# The National Australian Tide Gauge Network

Belinda Ronai

National Tidal Facility Australia, Flinders University of South Australia.

The National Australian Tide Gauge Network is made up of contributions from an array of tide gauges that have been maintained by NTF Australia as part of the ongoing Australian Baseline Sea Level Monitoring Project (ABSLMP) and gauges that belong to the Australian Association of Ports and Marine Authorities (AAPMA). NTF Australia maintains the quality controlled data output from these gauges for use in tidal analysis, prediction and research.

The Australian Baseline Array is comprised of fourteen SEAFRAME stations; Darwin, Broome, Hillarys, Esperance, Thevenard, Port Stanvac, Portland, Burnie, Spring Bay, Port Kembla, Rosslyn Bay, Cape Ferguson, Groote Eylandt and Cocos (Keeling) Islands. Each station records values of sea level, wind speed, direction and gust, air and water temperature and atmospheric pressure. Two sea level sensors are deployed for each station, a primary (AQUATRAK) sensor and a backup pressure sensor in the event of any problems with the primary. Sea level is monitored at six-minute intervals while the meteorological and temperature data is recorded at hourly intervals.  All SEAFRAME sites are surveyed regularly to ensure datum consistency and the results are published by AUSLIG on the Internet.

In addition to the above stations, NTF Australia has access to two stations in Victoria (Lorne and Stony Point) for inclusion in the Baseline Array. These stations are customised versions of the full SEAFRAME stations and are funded by the Victorian Channels Authority, whose cooperation is gratefully acknowledged.

Data is downloaded daily from each SEAFRAME gauge via a modem connection.  These downloads are monitored on a daily basis and any problems arising can be quickly identified and then rectified.  Hopefully within the next year or so the data acquisition system will be upgraded so that we may retrieve the data via satellite connections.

Data retrieved is subject to extensive quality control procedures on a regular basis, which check for timing errors, remove spikes and identify data gaps. Overall, the quality of the data retrieved from the SEAFRAME stations continues to be excellent.

Monthly reports on the data are produced and distributed and are generally available within two weeks of the end of each month, in hard copy form, and on the Internet.  These reports provide time series plots of all data output from the SEAFRAME stations, along with various other derived parameters, such as anomalies, trends and mean sea levels.  Please see the following web address for the latest monthly report.

http://www.ntf.flinders.edu.au/TEXT/PRJS/BASE/MRPTS/baseline.html

All observed and derived data output from the ABSLMP SEAFRAME stations is available on the NTF Australia website database.  This database is updated on a monthly basis and is easily accessible.  Please see the following web address:

http://www.ntf.flinders.edu.au/TEXT/WOCE/baseline.html

Tide gauge data not part of the ABSLMP is supplied to NTF Australia on an irregular basis each year for quality control, processing and analysis.  In total there are about 65 sea level data sets supplied from various locations around Australia as part of the tidal contract between AAPMA and NTF Australia.  NTF maintains the AAPMA tidal data for use in tidal analysis, prediction and research.  The sea level data is available by request.  Please see the following web address:

http://www.ntf.flinders.edu.au/TEXT/WOCE/aapma.html

One of the most important uses of sea level data from the National Australian Tide Gauge Network is in its use for determining estimates of sea level rise.  Data records need to be at least 25 years in length to produce realistic sea level trend estimates.  Thus, data from the SEAFRAME gauges part of the ABSLMP needs to be augmented with historical data from conventional gauges for trend analysis.  Research has been undertaken by NTF Australia into estimates of the overall average Australian sea level trend (+0.3 mm/year) in the following two papers.

Australian Mean Sea Level Survey:

http://www.ntf.flinders.edu.au/TEXT/PRJS/BASE/meansea.html

Sea Level Rise in Australia and the Pacific:

http://www.ntf.flinders.edu.au/TEXT/CONF/cook2000/papers/billdoc.pdf

Following is a listing of the hourly sea level data sets part of the National Australian Tide Gauge Network supplied by NTF Australia to the Fast Delivery WOCE Dataset on a monthly basis:

| GLOSS Number | Station name | Latitude | Longitude | Project | Observation Periods | Authority responsible for tide gauge |
| --- | --- | --- | --- | --- | --- | --- |
| 046 | Cocos Is. (Keeling) | 12°07'S | 096°53'E | Baseline | Float gauge 1985-1994; Acoustic gauge 1992- | NTF Australia |
| 060 | Townsville | 19°15'S | 146°50'E | AAPMA | 1948-; Digital data 1959- | Townsville Port Authority |
| 059 | Burnett Heads (Bundaberg) | 24°46'S | 152°23'E | AAPMA | 1966- | Bundaberg Port Authority |
| 058 | Brisbane (West Inner Bar) | 27°22'S | 153°10'E | AAPMA | 1957-8; 1966- | Marine Operations Branch Queensland Department of Transport |
| 057 | Sydney, Fort Denison | 33°51'S | 151°14'E | AAPMA | 1885- | Sydney Ports Corporation |
| 056 | Spring Bay | 42°33'S | 147°56'E | Baseline | Float gauge 1968-1969; Acoustic gauge 1991- | NTF Australia |

| GLOSS Number | Station name | Latitude | Longitude | Project | Observation Periods | Authority responsible for tide gauge |
| --- | --- | --- | --- | --- | --- | --- |
| 055 | Portland | 38°20'S | 141°36'E | Baseline | Float gauge 1982-1993; Acoustic gauge 1991- | NTF Australia |
| 308 | Thevenard | 32°10'S | 133°40'E | Baseline | Float gauge 1964-1993; Acoustic gauge 1992- | NTF Australia |
| 054 | Esperance | 33°52'S | 121°54'E | Baseline | Float gauge 1965-; Acoustic gauge 1992- | NTF Australia Deptment of Transport Marine Division WA |
| 040 | Broome | 18°00'S | 122°13'E | Baseline | Float gauge 1966-; Acoustic gauge 1991- | NTF Australia Deptment of Transport Marine Division WA |
| 062 | Darwin | 12°28'S | 130°51'E | Baseline | Float gauge 1958-; Acoustic gauge 1990- | Darwin Port Authority NTF Australia |

The remaining National Australian Tide Gauge Network datasets maintained by NTF Australia not supplied to the Fast Delivery WOCE Dataset are listed in the following table:

| ANTT Number | Station name | Latitude | Longitude | Project | Observation Periods |
| --- | --- | --- | --- | --- | --- |
| 46290 | Christmas Is. | 10°25'S | 105°40'E |  | Sep 1986 - Mar 1988, Aug 1990 - Nov 1991 |
| 57700 | Norfolk Is. | 29°04'S | 167°57'E |  | 1985- |
| 57720 | Lord Howe Is. | 31°31'S | 159°04'E |  | 1953-1956, 1957-1977, 1991- |
| 58100 | Twin Island | 10°28'S | 142°26'E | AAPMA | 1974 – 1975 |
| 58140 | Ince Point | 10°30'S | 142°19'E | AAPMA | 1971, 1974-1976, 1988 – |
| 58170 | Thursday Island | 10°35'S | 142°13'E | AAPMA | 1983 – |
| 58180 | Turtle Head (Hammond Island) | 10°31'S | 142°13'E | AAPMA | 1971, 1974-1976, 1989 – |
| 58180.1 | Hammond Rock Lighthouse |  |  | AAPMA | 1971, 1974–1976 |
| 58200 | Goods Island | 10°34'S | 142°10'E | AAPMA | 1974–1976, 1989 – |
| 58230 | Booby Is. | 10°36'S | 141°55'E | AAPMA | 1970- |
| 59040 | Port Douglas | 16°29'S | 145°28'E | AAPMA | 1978, 1987 – |
| 59060 | Cairns | 16°55'S | 145°47'E | AAPMA | 1960, 1966–1976, 1978, 1982, 1985 – |
| 59140 | Mourilyan Harbour | 17°36'S | 146°07'E | AAPMA | 1984 – |
| 59200 | Lucinda Offshore | 18°31'S | 146°23'E | AAPMA | 1985 – |
| 59260 | Cape Ferguson | 19°17'S | 147°03'E | Baseline | 1991 – |
| 59300 | Abbot Point | 19°51'S | 148°07'E | AAPMA | 1985–1995 |
| 59410 | Shute Harbour | 20°17'S | 148°47'E | AAPMA | 1982–1984, 1986 – |
| 59450 | Bugatti Reef | 20°05'S | 150°18'E | AAPMA | 1982–1983, 1996–1997 |
| 59510 | Mackay Outer Harbour | 21°07'S | 149°14'E | AAPMA | 1960, 1966–1979, 1984 – |
| 59511 | Hay Point | 21°16'S | 149°19'E | AAPMA | 1969, 1985 – |
| 59670 | Rosslyn Bay | 23°10'S | 150°47'E | Baseline | 1993 – |
| 59690 | Port Alma | 23°35'S | 150°52'E | AAPMA | 1985– |
| 59750 | Gladstone | 23°50'S | 151°15'E | AAPMA | 1978 – |
| 59840 | Fraser Island (Waddy Point) | 24°58'S | 153°21'E | AAPMA | 1976–1977 |
| 59850 | Urangan | 25°17'S | 152°55'E | AAPMA | 1996– |
| 59940 | Noosa Head | 26°23'S | 153°06'E | AAPMA | 1970–1973 |
| 59950 | Mooloolaba | 26°41'S | 153°07'E | AAPMA | 1979-1980, 1986 – |
| 59980 | Brisbane (West Inner Bar) | 27°22'S | 153°10'E | WOCE | 1957-8; 1966- |
| 60050 | Gold Coast Seaway | 27°57'S | 153°25'E | AAPMA | 1986 – |
| 60130 | Yamba | 29°25'S | 153°21'E | AAPMA | 1989 – |
| 60310 | Newcastle | 32°56'S | 151°47'E | AAPMA | 1957–1958, 1966 – |
| 60390 | Botany Bay | 33°59'S | 151°13'E | AAPMA | 1981–1997, 2000 – |
| 60420 | Port Kembla | 34°29'S | 150°55'E | Baseline | 1991 – |
| 60420.1 | Port Kembla | 34°29'S | 150°55'E | AAPMA | 1957 – 1993 |
| 60530 | Eden | 37°04'S | 149°54'E | AAPMA | 1957–1958, 1960–1972, 1983–1984, 1989 – |
| 60610 | Rabbit Island (Port Welshpool) | 38°55'S | 146°31'E | AAPMA | 1984–1985 |
| 60710 | Stony Point | 38°22'S | 145°13'E | Baseline | 1993 – |
| 60710.1 | Western Port (Stony Point) | 38°22'S | 145°13'E | AAPMA | 1963–1965, 1967–1968, 1981–1992 |
| 60720.1 | Hovell Pile | 38°19'S | 144°53'E | VCA | 1991– |
| 60726 | West Channel Pile | 38°11'S | 144°48'E | AAPMA | 1991– |
| 60730 | Port Phillip Heads (Point Lonsdale) | 38°18'S | 144°37'E | VCA | 1962– |
| 60740.1 | Queenscliff | 38°16'S | 144°39'E | VCA | 1991– |
| 60770 | Geelong (Port Phillip Bay) | 38°09'S | 144°22'E | AAPMA | 1965–1967, 1969 – |
| 60780 | Melbourne Williamstown | 37°52'S | 144°55'E | AAPMA | 1966 – |
| 60790 | Lorne | 38°30'S | 143°59'E | Baseline | 1993 – |
| 60900 | Stanley | 40°46'S | 145°18'E | AAPMA | 1965–1969 |
| 60910 | Burnie | 41°03'S | 145°57'E | Baseline | 1992 – |
| 60910.1 | Burnie | 41°03'S | 145°57'E | AAPMA | 1952–1956, 1965–1976, 1984–1991 |
| 60930 | Mersey River Devonport | 41°11'S | 146°22'E | AAPMA | 1965–1971, 1974–1976, 1989–1990, 1994 – |
| 60950 | Georgetown | 41°07'S | 146°49'E | AAPMA | 1965–1997 |
| 61220 | Hobart | 42°53'S | 147°20'E | AAPMA | 1960, 1962–1980, 1985, 1987 – |
| 61410 | Portland | 38°20'S | 141°36'E | Baseline | Float gauge 1982-1993; Acoustic gauge 1991- |
| 61460.1 | Cape Jaffa | 36°57'S | 139°40'E | AAPMA | 1980–1984 |
| 61490 | Victor Harbor | 35°34'S | 138°38'E | AAPMA | 1964– |
| 61583 | Port Stanvac | 35°06'S | 138°28'E | Baseline | 1992 – |
| 61600 | Port Adelaide Outer Harbor | 34°47'S | 138°29'E | AAPMA | 1940 – |
| 61600.1 | Port Adelaide Inner Harbor | 34°47'S | 138°29'E | AAPMA | 1960, 1966–1979, 1984 – |
| 61685 | Port Giles | 35°02'S | 137°46'E | AAPMA | 1982, 1994 – |
| 61780 | Wallaroo | 33°54'S | 137°36'E | AAPMA | 1976, 1980, 1982 – |
| 61800 | Port Pirie | 33°10'S | 138°01'E | AAPMA | 1917, 1920, 1930, 1932–1934, 1936–1938, 1940 – |
| 61840 | Whyalla | 33°01'S | 137°36'E | AAPMA | 1974, 1987 – |
| 61900 | Port Lincoln | 34°43'S | 135°52'E | AAPMA | 1964 – |
| 62000 | Thevenard | 32°10'S | 133°40'E | Baseline | Float gauge 1964-1993; Acoustic gauge 1992- |
| 62120 | Albany | 35°02'S | 117°53'E | AAPMA | 1960, 1966 – |
| 62190 | Bunbury | 33°19'S | 115°39'E | AAPMA | 1963–1964, 1966–1986 |
| 62230 | Fremantle | 32°03'S | 115°44'E | AAPMA | 1893- |
| 62237 | Hillarys Boat Harbour | 31°49'S | 115°44'E | Baseline | 1991 – |
| 62290 | Geraldton | 28°47'S | 114°35'E | AAPMA | 1963 – |
| 62341 | Denham | 25°56'S | 113°32'E | AAPMA | 1979–1980 |
| 62370 | Carnarvon | 24°54'S | 113°39'E | AAPMA | 1965- |
| 62435 | Exmouth | 21°56'S | 114°09'E | AAPMA | 1989–1993, 1998 – |
| 62470 | Onslow Beadon Creek | 21°39'S | 115°08'E | AAPMA | 1985 – |
| 62475 | Thevenard Island | 21°28'S | 115°01'E | AAPMA | 1987–1991 |
| 62490 | Barrow Island | 20°44'S | 115°28'E | AAPMA | 1990–1991 |
| 62491 | Barrow Island Off Shore | 20°49'S | 115°33'E | AAPMA | 1979 |
| 62540 | Dampier King Bay | 20°38'S | 116°45'E | AAPMA | 1982 – |
| 62540.1 | Dampier |  |  | AAPMA | 1966–1984 |
| 62550 | Port Walcott (Cape Lambert) | 20°35'S | 117°11'E | AAPMA | 1972, 1983 – |
| 62590 | Port Hedland | 20°19'S | 118°34'E | AAPMA | 1960; 1966- |
| 62650 | Broome | 18°00'S | 122°13'E | Baseline | Float gauge 1966-; Acoustic gauge 1991- |
| 62780 | Derby | 17°17'S | 123°36'E | AAPMA | 1982–1984 |
| 62860 | Yampi Sound (Koolan Island) | 16°08'S | 123°44'E | AAPMA | 1983–1985 |
| 63090 | Wyndham | 15°27'S | 128°06'E | AAPMA | 1966–1982, 1984 – |
| 63480 | Gove Harbour (Melville Bay) | 12°13'S | 136°42'E | AAPMA | 1965–1972, 1980 – |
| 63511 | Milner Bay | 13°50'S | 136°30'E | Baseline | 1993 – |
| 63511.1 | Milner Bay Groote Eylandt | 13°50'S | 136°30'E | AAPMA | 1966, 1971–1977, 1980–1987 |
| 63520 | Centre Island | 15°42'S | 136°54'E | AAPMA | 1966–1987 |
| 63540 | Mornington Island | 16°40'S | 139°10'E | AAPMA | 1976–1977 |
| 63580 | Karumba | 17°30'S | 140°50'E | AAPMA | 1985 – |
| 63620 | Weipa (Humbug Point) | 12°40'S | 141°53'E | AAPMA | 1966–1973, 1979–1980, 1984 – |