Report to the Ninth Session of the IOC Group of Experts

On the Global Sea Level Observing System (GLOSS)

Chilean  Sea Level Network: Current State

Juan J. Fierro

Servicio Hidrográfico y Oceanográfico de la Armada de Chile (SHOA)

#### Introduction

Since 1941, the Hydrographic and Oceanographic Service of the Chilean Navy (SHOA) has established a sea level network that actually comprises 19 sea level recorders covering a long coast of more than 4000 kilometers in the mainland, as well as in some islands and in the Antarctic Continent (see fig.1).

During 1999 an extensive hardware upgrading process was initiated. It considered the deployment of 18 data collecting platforms with satellite transmission data capabilities (VAISALA model 555C) and 1 self-contained platform (AANDERAA model 3634) that replaced most of the old dry purged recording tide gauge. At the moment, Rada Covadonga, (Lat. 63º 19’S  ;  Long.  57º 55’W) is the only sea level station  operating with AANDERAA devices.

Figure 1 :  Chilean Sea Level Network

Rada Covadonga Sea Level Station

Chile has conducted sea level observations in the Antarctica since 1947, initially with the installation of short period stations during summer, giving rise to records of greater extension once the experience in the installation and operation of tide instruments in this hostile environment was acquired. Therefore,  in 1983, tide gauge station Puerto Soberania (Base Prat) was settled which operating uninterruptedly became part of the national tide gauge network until the cease of its operation in January , 2004.

The greater facilities found for the installation and maintenance of tide instruments, determined the transfer of implements to Bernardo O’Higgins Antarctic Base located in Rada Covadonga. This station was incorporated in December, 2004 to the national tide gauge network replacing the old station of Puerto Soberanía. The maintenance of this station will be carried out annually during the hydrographic campaigns that are developed in the Antarctica. Figure 2 shows a view of the Base and pier in which the tide instrument was installed.

Previous sea level observations in this location were collected in 1975 during the experimental operation of tide instruments together with other short period observations obtained during some more recent hydrographic campaigns.

Figure 2 :  Rada Covadonga Antarctic Base.

### Status of GLOSS Stations in Chile

The eight Chilean stations that have been considered in the GLOSS core network are as follows :

| GLOSS ID. | Location | Status |
| --- | --- | --- |
| 137 | I. Pascua Lat : 27º 09’ S Lon: 109º 27’ W | Field Unit : Currently VAISALA 555C Sea Level Sensor : Currently Differential Pressure Transducer DRUCK PTX 1830 Two acoustic sensors Aquatrak Record Spans : 1970 – 2003 Gaps : 1980 ; 1982 ; 1983 Monthly Height Data up to 2002, has been sent to PSMSL Hourly Height Data up to 2002, has been sent to UHSLC |
| 74 | Antofagasta Lat : 23º 39’ S Lon: 70º 24’ W | Field Unit : Currently VAISALA 555C Sea Level Sensor : Currently Differential Pressure Transducer DRUCK PTX 1830 Record Spans : 1970 – 2003 Gaps : Monthly Height Data up to 2002, has been sent to PSMSL Hourly Height Data up to 2002, has been sent to UHSLC |
| 175 | Valparaíso Lat : 33º 02’ S Lon: 71º 37’ W | Field Unit : Currently VAISALA 555C Sea Level Sensor : Currently Differential Pressure Transducer DRUCK PTX 1830 Two acoustic sensors Aquatrak Record Spans : 1944 – 2003 Gaps : 1971 - 1981 Monthly Height Data up to 2002, has been sent to PSMSL Hourly Height Data up to 2002, has been sent to UHSLC CGPS data up to 2004, has been sent to UH-IGP |
| 176 | I.J.Fernández Lat : 33º 37’ S Lon: 78º 50’ W | Field Unit : Currently VAISALA 555C Sea Level Sensor : Currently Differential Pressure Transducer DRUCK PTX1830 Record Spans : 1985 – 2003 Gaps : Monthly Height Data up to 2002, has been sent to PSMSL Hourly Height Data up to 2002, has been sent to UHSLC |
| 177 | I.San Félix Lat : 26º 17’ S Lon: 80º 07’ W | Field Unit : Currently VAISALA 555C Sea Level Sensor : Currently Differential Pressure Transducer DRUCK PTX 1830 Record Spans : 1989 – 2003 Gaps : Monthly Height Data up to 2002, has been sent to PSMSL Hourly Height Data up to 2002, has been sent to UHSLC |

| GLOSS ID. | Location | Status |
| --- | --- | --- |
| 178 | P.Montt Lat : 41º 29’ S Lon: 72º 58’ W | Field Unit : Currently VAISALA 555C Sea Level Sensor : Currently Differential Pressure Transducer DRUCK PTX 1830 Record Spans : 1945 – 2003 Gaps : Monthly Height Data up to 2002, has been sent to PSMSL Hourly Height Data up to 2002, has been sent to UHSLC |
| 180 | I.D.Ramírez Lat : 56º 30’ S Lon: 68º 43’ W | Non – Operational (closed in 1998) Record Spans : 1991 – 1997 Gaps : Monthly Height Data up to 1997, has been sent to PSMSL Hourly Height Data up to 1997, has been sent to UHSLC |
| 189 | P. Soberanía (Base Prat) Lat : 62º 29’ S Lon: 59º 38’ W | Non – Operational (closed in January 2004) Record Spans : 1984 – 2003 Gaps : Monthly Height Data up to 2002, has been sent to PSMSL Hourly Height Data up to 2002, has been sent to UHSLC |

Remarkable issues

GLOSS 137

Eastern Island holds our standard configuration of sensors and also has been equipped with two acoustic sensors since 2002 under responsability of the University of Hawaii.

During 2004 it has operated with gaps as a result of power supply problems.

GLOSS 174

An ultrasonic wind sensor has been incorporated during the last semester  of 2004.

GLOSS 175

Valparaíso holds our standard configuration of sensors. This station is also equiped with a shaft encoder and two acoustic sensors since 1998 under responsability of the University of Hawaii.

GLOSS 180

Diego Ramirez Island is a non-operational station. Equipment was removed during 1998 after informing NOAA about logistic problems in maintaining SHOA’s permanent personnal staff in this island.

GLOSS 189

Puerto Soberanía is a non-operational station. The Aanderaa instrument was removed in January 2004 as mentioned above.

Data Streams

Chile contributes to GLOSS maintaining adecuate data streams to GLOSS archiving Centres.

We have delivered the data up to 2002 according the 4 main data streams in GLOSS:

- Monthly mean Sea Level to PSMSL

- Hourly Heights in delayed mode to UHSLC

- Fast Higher frequency to UHSLC

Data collected at all the Chilean stations are being downloaded in near real-time by UHSLC.

- GPS data collected in Valparaíso station (GLOSS 175) are sent to University of Hawaii.

Future Plans

The installation during 2005 at SHOA’s facilities of a VAISALA Direct Readout Ground Station (DRGS).

Once the technical details have been evaluated, we will schedule the installing at San Pedro sea level station (Lat. 47º 44’S ; Long. 74º 54’W) of a secondary sea level sensor which probably could be a KALESTO radar sensor. Since its installation in 1995, this station has operated with several interruptions, mainly due to the short daily radiation to provide adequate energy for battery charging and also to damages suffered by the DRUCK sensor which is frequently cut because of sea storm in this part of the Chilean coast.