The United States National Report

Contributions to GLOSS

Michael Szabados, Director

NOAA National Ocean Service

Center for Operational Oceanographic Products and Services

The United States National Report

Contributions to GLOSS

Table of Contents

Components of the U.S. National Program in Support of GLOSS

Introduction

A) The NOAA Office of Global Programs Project Office for Climate Observations 	Activities

B) The NOAA National Ocean Service National Water Level Program Status

1. Operational Status of NOAA National Ocean Service Tide Stations in 			Support of GLOSS Activities

2. Planned Efforts to Upgrade NOAA Tide Stations to Support the U.S. 			Tsunami Warming Program

3. Sea Level Trends Product Enhancement

4. Upgrade of NOAA Ocean Island Station Operations

5. Satellite Altimeter Mission Support

6. The U.S. Climate Change Science Program

7. U.S. Contributions to the Integrated Ocean Observing System (IOOS)

C) The University of Hawaii Sea Level Center Status

1. The joint Archive for Sea Level (JASL)

2. The Fast Delivery Database

3. Near Real-Time Data

APPENDIX 1. NOAA’s Climate Observations Program Description

APPENDIX 2. NOAA’s National Water Level Program Description

APPENDIX 3.  University of Hawaii Sea Level Center Program Description

The United States National Report

Contributions to GLOSS  - DRAFT 2/8/05

Michael Szabados, Director

NOAA National Ocean Service

Center for Operational Oceanographic Products and Services

Components of the U.S. National Program in Support of GLOSS

Introduction

This United States National Report is a summary of the operational water level observation programs in the United Sates that provide support to GLOSS and the international community.  The three major components of this support are:

- The U. S. National Oceanic and Atmospheric Administration (NOAA) Office of 	 Global Programs Project Office for Climate Observations,

- The NOAA National Ocean Service National Water Level Program managed by the Center for Operational Oceanographic Products and Services, and

- The University of Hawaii Sea Level Center

A)  The NOAA Office of Global Programs Project Office for Climate Observations Activities

The goal of the program  (http://www.oco.noaa.gov/)  is to build and sustain the ocean component of a global climate observing system that will respond to the long term observational requirements of the operational forecast centers, international research programs, and major scientific assessments. The program objectives are to:

- document long term trends in sea level change;

- document ocean carbon sources and sinks;

- document the ocean’s storage and global transport of heat and fresh water;

- document ocean-atmosphere exchange of heat and fresh water.

The ocean is the memory of the climate system and is second only to the sun in effecting variability in the seasons and long-term climate change. In order for NOAA to fulfill its climate mission, the global ocean must be observed. At present, the Climate Observation Program is arguably the world leader in supporting implementation of the in situ elements of the global ocean climate observing system.

Present ocean observations are not adequate to deliver these products with confidence. The fundamental deficiency is lack of global coverage by the in situ networks. Present international efforts constitute only about 45% of what is needed in the ice-free oceans and 11% in the Arctic. The Second Report on the Adequacy of the Global Observing System for Climate in Support of the UNFCCC concludes that “the ocean networks lack global coverage and commitment to sustained operations…Without urgent action to address these findings, the Parties will lack the information necessary to effectively plan for and manage their response to climate change.” The Strategic Plan for the U.S. Climate Change Science Program calls for “complete global coverage of the oceans with moored, drifting, and ship-based networks.” The draft Ocean.US interagency plan for Implementation of the Initial U.S. IOOS specifies that “the highest priority for the global component of the IOOS is sustained, global coverage.”

The recent Earth Observation Summit raised to the highest levels of governments the awareness of the need for a global observation system. The climate question is high on the political agendas of many nations and can be answered authoritatively only by sustained earth observation. The Earth Observation Summit reaffirmed NOAA’s leadership and commitment to fulfilling the need for global coverage and the Climate Observation Program is NOAA’s management tool for implementing the ocean component.   Appendix 1 is a more detailed description of the Climate Observation Program activities.

B)  The NOAA National Ocean Service National Water Level Program Status

1. Operational Status of NOAA National Ocean Service Tide Stations in Support of GLOSS Activities

The Tides and Currents Programs, managed by the NOAA National Ocean Service (NOS) Center for Operational Oceanographic Products and Services (CO-OPS), are used to support the statutory mandates and all NOAA missions.  The NOAA National Water Level Program (NWLP), the National Current Observation Program (NCOP), and the Physical Oceanographic Real-Time System (PORTS®) are fundamental coastal ocean observing system programs (http://tidesandcurrents.noaa.gov/).  The NWLP is an “end-to-end” system of data collection, quality control, data management, and product delivery with a long-term network of continuously operating stations, the National Water Level Observation Network (NWLON) at the core.  The NWLP and its methodologies and standard operating procedures for data collection and production of tidal and water level datum products are seen as national standards for certification of information for legal applications and for technology transfer.  The program is seen as a national authority and NOAA accepts responsibility for the accuracy of its products.   Appendix 2. is a detailed description of the NWLP.

Table 1 is a listing of the tide stations operated by NOAA contributing to the GLOSS network.  Notes include the latest entries into the GLOSS database, the type of primary sensor in operation, and the latest date of contribution to the JASL archive database.   There are 29 of the 175 NOAA NWLON stations on this list.  Table 2 is a listing of the tide stations operated by NOAA that are contributing to the JASL archive data base at the present time.  All of the GLOSS stations in Table 1 contribute to the JASL database.  There are 54 total NOAA operational NWLON stations that actively contribute to the JASL archive.  The 18 stations identified at the 1997 International Sea Level Workshop as critical to the global system for monitoring long term sea level trends are also identified in the tables as CRN stations.

2. Planned Efforts to upgrade NOAA tide stations to support the U.S. tsunami warning program.

Xpert General System Operations: The planned Data Collection Platform (DCP) upgrades will include replacing both the primary and redundant DCPs. Each of the NWLON stations has both a primary and redundant (backup) system to help assure continuous data records. The new primary DCP will be equipped with a high-data-rate GOES transmitter which will be operating at 300 baud and the systems will transmit data via GOES every 6 minutes. Each message will contain the most recent water level (WL) measurement from both the primary and redundant systems including data quality parameters (mean, std dev, outliers, for both, and 2 temperature measurements for acoustic sensor). The message will also include data from any meteorological sensors that might be installed at the station, as well as the preceding 6 minute WL measurements from primary and redundant sensors which can be used to fill data gaps should a transmission be missed.

Xpert Tsunami Upgrade for continuous one minute water level data:  For stations identified as “tsunami”, the primary DCP will compute 1 minute WL averages and store the most recent 30 days of this higher frequency data. In addition, the most recent 6 - 1 minute WL measurements would be added to the standard GOES message. This would provide continuous 1 minute data sets from these stations every 6 minutes.

Xpert Tsunami Upgrade for 15 second water level data:  For stations identified as “tsunami”, the redundant DCP would also be configured to compute and store 15 second WL averages from its pressure based sensor and, as with the primary DCP, the most recent 30 days of this high frequency data would be stored at the DCP on a flash memory card. The 15 second average is the scheme used with the present Sutron 9000/8200 based systems. The data rate could be increased slightly, perhaps 10 second averages, however, this provides extremely noisy data. This data can be retrieved by phone (we will have phone access to both primary and redundant systems) via the system's 56K modem which should provide relatively quick downloads. This data could be retrieved by visiting the station and removing the flash memory card.  A third method of accessing the 15 second data will be through the installation of an IP cellular modem.  This enables a data collection computer to launch numerous simultaneous telnet sessions when a seismic event occurs and would provide real-time 15 second water level data from stations in the path of a potential tsunami wave.

Planned new NOAA NWLON Stations in Support of the U.S. Tsunami Warning System:  In response to the recent tsunami disaster in the Indian Ocean, the U.S. has been evaluating its national tsunami warning system.  Based on the evaluation, resources are being targeted towards enhancement of the operational tide gauges used as part of the warning network.  Several new stations are being deployed by NOAA over the next few years as summarized in Figures 1 and 2.

Figure 1.  NOAA NWLON Operational Status

Figure 2. NOAA NWLON Operational Status – Pacific Region

3.  Sea level Trends Product Enhancement

There are 18 NOAA National Water Level Observation Network (NWLON) stations identified in the International Sea Level Workshop Report (1997) as being part of the core global subset for long term trends.  The NOAA Climate Observations Program Plan calls these climate "reference stations" and includes the following performance measures for the reference stations:

1. Routinely deliver an annual report of the variations in relative annual mean sea level for the entire length of the instrumental record.

2. Routinely deliver an annual report of the monthly mean sea level trend for the past 100 years with 95% confidence interval.

The Climate Observation Program will be producing an annual report on the state of the ocean and the state of the observing system for climate.  It is proposed that an annual report on these reference stations that would be one section of that larger report.  Over the next 3 years it is required that the report include all 62 global reference stations.   The current NOAA report on sea level is being used as a starting template for an annual report.

NOAA began the development efforts for an annual report that includes the 18 NWLON stations listed above.  A tailored version of the graphics and analyses from the existing NOAA sea level report has been completed that includes the three fundamental types of analyses where data series allow.  The following figures illustrate the types of analyses using Honolulu as an example.

Figure 1.  Sea level Trends Analyses would be updated annually.

Figure 2.  Long-term Variation in Trends would be routinely updated.

Figure 3.  The Monthly Mean Sea Level variations would be updated annually.

CO-OPS will extend the compilation of the data and the reports from the 18 NWLON stations to include all 62 global reference stations assuming routine data availability each year.  Efforts will concentrate on getting the data compiled in a timely fashion and generating routine reports established in the first year effort.  Success will depend upon the ability to get timely data from all stations.  These efforts will be coordinated with PSMSL, GLOSS and UHSLC programs.

4.  Upgrade of NOAA Ocean Island Station Operations

There are several coastal and island NWLON stations critical to the Global Climate Observing System.  The operation and maintenance of the ocean island stations of the National Water Level Observation Network (NWLON) has been increasingly more difficult over time due to the slow abandonment of the island facilities at which the stations reside.  Finding routine flights and flights which are cost effective are becoming increasingly difficult, yet these stations require high standards of annual maintenance to ensure the integrity of their long term data sets.  Annual maintenance is even more important, in light of the fact that corrective maintenance is logistically very difficult and expensive.

Although operation of all of the stations is important, it is proposed that Ocean Island stations begin to be upgraded first with this funding to ensure their continuous operation (program funding and budget initiatives will be used for operation of the coastal stations).  These targeted funds will be used for travel costs and for upgrade to backup systems.  The upgrades will include high accuracy acoustic or paroscientifc pressure sensors and redundant Data Collection Platforms (DCP’s) with equal capability to the existing primary systems.  The station operations will also be enhanced with GPS connections to geodetic systems followed by installation of  GPS Continuously Operating Reference Systems (CORS) at selected sites.  The following is a list of the ocean island NWLON stations (not including Hawaii) that will considered in this category as priority for upgrade.

Station:		CORS Operating

Guam		Yes

Kwajalein		Yes

Pago Pago		Yes

Wake		No

Midway		No

Adak		No

Bermuda		Yes

San Juan. PR		Yes

Magueyes Island, PR		No

Charlotte Amalie, VI		No

St Croix, VI		Yes

Upgrades will be completed a two critical ocean island stations at Midway and at Guam in 2005.

5.  Satellite Altimeter Mission Support

Support for the TOPEX/Poseidon satellite altimeter mission began with installation of an acoustic system and a digibub system on Platform Harvest in 1983 .  Using reimbursable funding under MOA with JPL/Caltech, systems operations include provision of water level measurements relative to the satellite altimeter closure analysis reference frame for calibration monitoring (see B. Hanes et al, Special Issue of Marine Geodesy, 2003 “The Harvest Experiment:  Monitoring Jason-1 and TOPEX-Poseidon from a California Offshore Platform”.

NOS special support has included a vertical survey on the Platform necessary to relate the water level sensor reference zeros (near the bottom catwalk) to the GPS reference zero (located up top at the helipad on the Platform.   Continuous data are required to monitor effects of waves on the water level measurements and to ensure provision of data during the times of altimeter overflights every ten days.  The original acoustic system was replaced by a digibub pressure system prior to the Jason-1 altimeter launch.  Platform Harvest tide gauge operations will continue with the operation of two digital bubbler pressure systems collecting continuous water level data streams surveyed into the Platform and Satellite Orbit Reference frames.

6.   The U.S. Climate Change Science Program

The U.S. President established the U.S. Climate Change Science Program (CCSP) in 2002 (http://www.climatescience.gov/).  In July 2003, the interagency Committee on Climate Change Science and Technology Integration disseminated two documents: The U.S. Climate Change Science Program: Vision for the Program and Highlights of the Scientific Strategic Plan and the complete Strategic Plan for the Climate Change Science Program.

Sea level is introduced in Chapter 9 of the Strategic Plan and addresses Human Contributions and Responses to Environmental Change. This Chapter was coauthored by the Environmental Protection Agency (EPA) and NOAA. Question 9.2 of this Chapter is posed as: What are the current and potential future impacts of global environmental variability and change on human welfare, what factors influence the capacity of human societies to respond to change, and how can resilience be increased and vulnerability reduced?  Two of the products/milestones are:

- Elevation maps depicting areas vulnerable to sea level rise and planning maps depicting how state and local governments could respond to sea-level rise (less than two years).

- Assessment of how coastal environmental programs can be improved to adapt to sea-level rise while enhancing economic growth (2 - 4 years).

The U.S. Environmental protection Agency (EPA) is currently listed as the lead for these deliverables and NOAA/National Ocean Service (NOS) is co-leading this effort.  NOS has been asked by NOAA management for a report on what it would take to produce these deliverables.  The NOAA Climate Office has specifically asked NOS for a report as soon as possible.  This document is a draft report on a sea-level deliverable that NOS could provide within the required time frame.

The deliverable would demonstrate how NOS would use the strength of existing partnerships with local communities, existing national infrastructure in surveying, mapping, and existing capabilities for sea level analyses.  The existing NOS effort in North Carolina would be used as a template to create a plan for a sea level rise deliverable for the nation.

7.  U.S. Contributions to the Integrated Ocean Observing System (IOOS)

The Integrated Ocean Observing System (IOOS) is envisioned as a coordinated national and international network of observations, data management and analyses that systematically acquires and disseminates data and information on past, present and future states of the oceans and the nation’s Exclusive Economic Zone Integrated Global Environmental Observation and Data Management.   Ocean observations are essential to NOAA’s mission and NOAA will lead development of observation and data management systems into an Integrated Ocean Observing System (IOOS). With partners here and abroad, NOAA will incorporate measurements on valuable hydrographic, geodetic, land cover, topographic, and water-level information. NOAA will foster regional collaborations for observing coastal conditions through the U.S. Federal interagency National Ocean Research Leadership Council and Ocean.US.  Using IOOS funding from the U.S. Congress, NOAA will be expanding the NWLON with a few stations in 2006 at key locations with data information gaps to meet all users’ needs for water level data.

C.   The University of Hawaii Sea Level Center Status

The University of Hawaii Sea Level Center (UHSLC) collects, processes, and distributes tide gauge measurements from around the world in support of various climate research activities.  Funding for the UHSLC is provided by the Office of Climate Observation (OCO), NOAA.  UHSLC data are used for the evaluation of numerical models, joint analyses with satellite altimeter datasets, the calibration of altimeter data, the production of oceanographic products through the WMO/IOC JCOMM Sea Level Program in the Pacific (SLP-Pac) program, and research on sea level rise and interannual to decadal climate fluctuations.  In support of satellite altimeter calibration and validation and for absolute sea level rise monitoring, the UHSLC and the Pacific GPS Facility maintain co-located GPS systems at select tide gauge stations (GPS@TG).  The UHSLC currently is a designated CLIVAR Data Assembly Center (DAC) and an IOC GLOSS data archive center.  The UHSLC distributes data directly from its own web site and through a dedicated OPeNDAP server.  The data are redistributed by the National Oceanographic Data Center (NODC), the Permanent Service for Mean Sea Level, the Climate Data Portal (CDP) maintained by the Pacific Marine Environmental Laboratory, the National Virtual Ocean Data System (NVODS), the International Pacific Research Center’s GODAE data server, and the NOAA Observing System Architecture (NOSA) web site.

The UHSLC operates 37 tide gauge stations in the global sea level network and collaborates with host countries in the operation of 7 more stations.  In the past year, HSLC serviced 13 sites, installed 1 new station, and serviced 16 sites remotely.  The historical data return for the UHSLC network is 93.8%, the current year's return is 95.3%, and the previous years return 96.8%.  The UHSLC in collaboration with the Pacific GPS Facility operates co- located continuous GPS (GPS@TG) receivers at 7 tide gauges, which constitute to the NASA/CNES Science Working Team for altimeter calibration, and provide local estimates of absolute sea level rise.

The UHSLC distributes three sea level data sets:

1) The Joint Archive for Sea Level (JASL) data set is designed to be user friendly, scientifically valid, well-documented, and standardized for archiving at international data banks. JASL data are provided internally by the UH Sea Level Network and by over 60 agencies representing over 70 countries.  In the past year, the UHSLC increased its JASL holdings to 10,007 station-years of hourly quality assured data.  The JASL set now includes 5617 station years of data in 264 series at 202 GLOSS sites.

2) The Fast Delivery Database supports various international programs, in particular CLIVAR and GCOS.  The database has been designated by the IOC as a component of the GLOSS program.  The fast delivery data are used extensively by the altimeter community for ongoing assessment and calibration of satellite altimeter datasets.  The fast delivery sea level dataset now includes 141 stations, 113 of which are located at GLOSS sites.

3) Near Real-Time Data (collection + up to a three hour delay, H-3 delay) and daily filtered values (J-2 delay) are provided by the UHSLC in support of GODAE.  Approximately 50 stations currently are available in real-time with plans for ongoing expansion.  When operational, we will distribute this product through our public web site, and make it available in a netCDF format via OPeNDAP server for use in forecast models and for satellite altimeter calibration.

The UHSLC provides monthly maps of the Pacific sea level fields through the JCOMM sponsored SLP-Pac.  UHSLC also produces quarterly updates of an index of the tropical Pacific upper layer volume and annual updates of indices of the ridge-trough system and equatorial currents for the Pacific Ocean.  The analysis includes tide gauge and altimeter sea surface elevation comparisons.

| Table 1: Status of GLOSS Stations in the United States operated by NOAA/NOS |
| --- |
| GLOSS ID | Location | Status |
| 111 | Kwajelein | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (055A) data through 2003 CRN station |
| 206 | San Juan, PR | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (245A) data through 2003 |
| 221 | Bermuda | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (259A) data through 2003 CRN station |
| 302 | Adak, AK | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (040A) data through 2003 |
| 149 | Apra Harbor, Guam | Ongoing, station being rebuilt after a typhoon, currently using a digital/pressure bubbler gauge – redundant DCP to be installed PSMSL data through 2002 JASL (053A) data through 2003 CRN station |
| 219 | Duck Pier, NC | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (260A) data through 2003 |
| 289 | Fort Pulaski, GA | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (752A) data through 2003 |
| 217 | Galveston Pier 21, TX | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JAS L(775A) data through 2003 |
| 287 | Hilo, HI | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (060A) data through 2003 |
| 108 | Honolulu. HI | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (057B) data through 2003 CRN station |
| 109 | Johnston Island | No longer operated by NOAA PSMSL data through 2002 JASL (052A) data through 2003 |
| 216 | Key West, FL | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (242A) data through 2003 CRN station |
| 159 | La Jolla, CA | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (569A) data through 2003 CRN station |
| 303 | Attu Island, AK | No longer operated by NOAA – station may be re-established using Tsunami funding in 2006 PSMSL data through 1966 JASL (550A) data through 1966 |
| 218 | Miami (Haulover Pier) | Destroyed in 1992 by hurricane – moved to Virginia Key, FL Ongoing, currently using an acoustic gauge with pressure gauge backup – station is not connected to datum at Miami so a new PSMSL station is needed. JASL Miami data through 1992 JASL (755A) Virginia Key data 1996 through 2003 |
| 106 | Midway Island | Ongoing, currently using an acoustic gauge with pressure gauge backup – redundant DCP to be installed in 2006. PSMSL data through 2002 JASL (050A) data through 2003 |
| 290 | Newport, RI | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (253A) data through 2003 |
| 74 | Nome, AK | Ongoing, currently using a dual orifice digital/bubbler system PSMSL data through 2002 JASL (0595A) data through 2001 |
| 144 | Pago Pago | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (056A) data through 2003 |
| 288 | Pensacola, FL | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (762A) data through 2003 CRN station |
| 151 | Prudhoe Bay, AK | Ongoing, currently using an acoustic gauge during the ice – free season and a digital/bubbler system during the winter PSMSL data through 2002 JASL (579A) data through 2003 |
| 158 | San Francisco, CA | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (551A) data through 2003 CRN station |
| 100 | Sand Point, AK | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (574A) data through 2001 |
| 150 | Seward, AK | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (560C) data through 2003 |
| 154 | Sitka, AK | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (559A) data through 2003 |
| 157 | South Beach, OR | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (592A) data through 2003 |
| 102 | Unalaska, AK | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (041B) data through 2003 |
| 220 | Atlantic City, NJ | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (264A) data through 2003 CRN station |
| 105 | Wake Island | Ongoing, currently using a acoustic gauge with pressure gauge backup PSMSL data through 2002 JASL (051A) data through 2003 |

| Table 2: Status of additional operational non- GLOSS JASL NWLON Stations in the United States |
| --- |
| JASL ID | Location | Status |
| 039A | Kodiak, AK | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 058A | Nawiliwili, HI | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 059A | Kahului, HI | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 061A | Mokuoloe, HI | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 552A | Kawaihae, HI | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 555A | Monterey, CA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 556A | Crescent City, CA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 CRN station |
| 557A | Port Orford, OR | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 558A | Neah Bay, WA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 CRN station |
| 561A | Seldovia, AK | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 562A | Valdez. AK | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 564A | Willapa Bay, WA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 565A | Port San Luis, CA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 567A | Los Angeles, CA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2001 |
| 570A | Yakutat, AK | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 571A | Ketchikan, AK | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 CRN station |
| 572A | Astoria, OR | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 573A | Arena Cove, CA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 575A | Charleston, OR | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 576A | Humboldt Bay, CA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 578A | Santa Monica, CA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 583B | Cordova, AK | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 594A | Platform Harvest, CA | Ongoing, currently two DCP’s with paroscientific pressure digital bubbler sensors JASL data through 1999 |
| 246A | Magueyes Island, PR | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 261A | Charleston, SC | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 CRN station |
| 240A | Fernandina Beach, FL | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 CRN station |
| 252A | Portland, ME | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 CRN station |
| 254A | Limetree bay, VI | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 255A | Charlotte Amalie, VI | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 279A | Montauk, NY | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 740A | Eastport, ME | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 741A | Boston, MA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 CRN station |
| 742A | Woods Hole. MA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 743A | Nantucket, MA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 744A | New London, CT | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 745A | New York, NY | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 CRN station |
| 746A | Cape May, NJ | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 747A | Lewes, DE | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 749A | Chesapeake BBT, VA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 750A | Wilmington, NC | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 753A | Mayport, FL | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 757A | Naples,FL | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 759A | St. Petersburg, FL | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 760A | Appalachicola, FL | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 761A | Panama City Beach, FL | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 763A | Dauphin Island, AL | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 765A | Grand Isle, LA | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 766A | Sabine Pass, TX | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 767A | Galveston Pleasure Pier, TX | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 769A | Rockport, TX | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 770A | Corpus Christi, TX | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 1999 |
| 772A | Port Isabel, TX | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 773A | Clearwater Beach FL | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
| 774A | Port Canaveral, FL | Ongoing, currently using a acoustic gauge with pressure gauge backup JASL data through 2003 |
|  | Hampton Roads, VA | CRN station for se level |

Table 3.  Stations for which the UHSLC operates or assists in the operations.  GPS@TG indicates which stations have UHSLC GPS co-located at the tide stations.

GLOSS STATION           COUNTRY           LAT    LONG

004  Salalah           Oman              16-56N 054-00E

xxx  Masirah           Oman              20-41N 058-52E

008  Mombasa           Kenya             04-04S 039-39E

xxx  Lamu              Kenya             02-16S 040-54E

018  Port Louis        Mauritius         20-09S 057-30E

019  Rodrigues         Mauritius         19-40S 063-25E

026  Diego Garcia      United Kingdom    07-17S 072-24E

027  Gan               Rep. of Maldives  00-41S 073-09E

028  Male,Hulule       Rep. of Maldives  04-11N 073-32E GPS@TG

xxx  Hanimaadhoo       Rep. of Maldives  06-46N 073-10E

033  Colombo           Sri Lanka         06-57N 079-51E

107  French Frigate S  USA               23-52N 166-17W

108  Honolulu          USA               21-18N 157-52W GPS@TG

109  Johnston          USA Trust         16-44N 169-32W

115  Pohnpei           Fd St Micronesia  06-59N 158-15E

117  Kapingamarangi    Fd St Micronesia  01-06N 154-47E

118  Saipan            N. Mariana Is.    15-14N 145-45E

119  Yap               Fd St Micronesia  09-31N 138-08E

120  Malakal           Rep. of Belau     07-20N 134-28E GPS@TG

123  Noumea            France            22-18S 166-26E

128  Chatham           New Zealand       43-57S 176-34E

137  Easter            Chile             27-09S 109-27W

138  Rikitea           French Polynesia  23-08S 134-57W

140  Papeete           French Polynesia  17-32S 149-34W

143  Penrhyn           Cook Islands      08-59S 158-03W

145  Kanton            Rep. of Kiribati  02-49S 171-43W

146  Christmas         Rep. of Kiribati  01-59N 157-28W

161  Cabo San Lucas    Mexico            22-53N 109-55W

163  Manzanillo        Mexico            19-03N 104-20W GPS@TG

169  Baltra            Ecuador           00-26S 090-17W

xxx  Santa Cruz        Ecuador           00-45S 090-19W

175  Valparaiso        Chile             33-02S 071-38W GPS@TG

xxx  Salvador          Brazil            12-58S 038-31W

181  Ushuaia           Argentina         54-48S 068-18W

185  Mar Del Plata     Argentina         63-24S 056-60W

211  Settlement Pnt.   Bahamas           26-41N 078-59W GPS@TG

245  Ponta Delgada     Portugal          37-44N 025-40W

xxx  Palmeira,C.Verde  Portugal          16-45N 022-59W GPS@TG

253  Dakar             Senegal           14-41N 017-25W

273  Pt. La Rue        Seychelles        04-40S 055-32E

297  Zanzibar          Tanzania          06-09S 039-11E

APPENDIX 1.  NOAA’s Climate Observations Program Description

Program Description (see http://www.oco.noaa.gov/)

Goal and Objectives: 
The goal of the program is to build and sustain the ocean component of a global climate observing system that will respond to the long term observational requirements of the operational forecast centers, international research programs, and major scientific assessments. The program objectives are to:

- document long term trends in sea level change;

- document ocean carbon sources and sinks;

- document the ocean’s storage and global transport of heat and fresh water;

- document ocean-atmosphere exchange of heat and fresh water.

Specific issues, requirements, and customer need motivating the program: 
The ocean is the memory of the climate system and is second only to the sun in effecting variability in the seasons and long-term climate change. In order for NOAA to fulfill its climate mission, the global ocean must be observed. At present, the Climate Observation Program is arguably the world leader in supporting implementation of the in situ elements of the global ocean climate observing system.

The observing system needs to have the capability to deliver continuous instrumental records and analyses accurately documenting:

- Sea level to identify changes resulting from climate variability.

- Ocean carbon content every ten years and the air-sea exchange seasonally.

- Sea surface temperature and surface currents to identify significant patterns of climate variability.

- Sea surface pressure and air-sea exchanges of heat, momentum, and fresh water to identity changes in forcing function driving ocean conditions and atmospheric conditions.

- Ocean heat and fresh water content and transports to identify where anomalies enter the ocean, how they move and are transformed, and where they re-emerge to interact with the atmosphere.

- The essential aspects of thermohaline circulation and the subsurface expressions of the patterns of climate variability.

- Sea ice thickness and concentrations.

Present ocean observations are not adequate to deliver these products with confidence. The fundamental deficiency is lack of global coverage by the in situ networks. Present international efforts constitute only about 45% of what is needed in the ice-free oceans and 11% in the Arctic. The Second Report on the Adequacy of the Global Observing System for Climate in Support of the UNFCCC concludes that “the ocean networks lack global coverage and commitment to sustained operations…Without urgent action to address these findings, the Parties will lack the information necessary to effectively plan for and manage their response to climate change.” The Strategic Plan for the U.S. Climate Change Science Program calls for “complete global coverage of the oceans with moored, drifting, and ship-based networks.” The draft Ocean.US interagency plan for Implementation of the Initial U.S. IOOS specifies that “the highest priority for the global component of the IOOS is sustained, global coverage.”

The recent Earth Observation Summit raised to the highest levels of governments the awareness of the need for a global observation system. The climate question is high on the political agendas of many nations and can be answered authoritatively only by sustained earth observation. The Earth Observation Summit reaffirmed NOAA’s leadership and commitment to fulfilling the need for global coverage and the Climate Observation Program is NOAA’s management tool for implementing the ocean component.

Partnerships: 
The Climate Observation Program is managed as an inter-LO, interagency, and international effort. Presently most NOAA contributions to the global system are being implemented by the OAR laboratories, joint institutes and university partners. NOS, NMFS, and NWS maintain observational infrastructure for ecosystems, transportation, marine services and coastal forecasting that do or have potential to contribute to climate observation. NOS sea level measurements in particular provide one of the best and longest climate records existent. NESDIS data centers are essential. NMAO ship operations are necessary for supporting ocean work. NESDIS and NPOESS continuous satellite missions are needed to provide the remote sensing that complements the in situ measurements.

International and interagency partnerships are central to the Climate Observation Program implementation strategy. All of the Program’s contributions to global observation are managed in cooperation internationally with the Joint WMO/IOC Technical Commission for Oceanography and Marine Meteorology (JCOMM), and nationally with the U.S. Integrated Ocean Observing System (IOOS). NSF has initiated their Ocean Observatories Initiative (OOI) which will potentially provide significant infrastructure in support of ocean climate observation, beginning in FY 2006. The ongoing NSF-NOAA cooperative project for CLIVAR-carbon ocean surveys has proved to be an interagency international-interdisciplinary success. ONR maintains a GODAE data server at Monterey that needs to be sustained after the experiment period (2003-2005) as permanent international infrastructure. The UNOLS fleet provides ship support for ocean operations. NASA’s development of remote sensing techniques is key.

Focus of the Program:

- Extending the in situ networks to achieve global coverage – moored and drifting buoys, profiling floats, tide gauges stations, and repeated ship lines.

- Building associated data and assimilation subsystems.

- Building observing system management and product delivery infrastructure.

APPENDIX 2.  NOAA’s National Water Level Program Description

1.  Overview (see http://tidesandcurrents.noaa.gov)

The Tides and Currents Programs, managed by the NOAA National Ocean Service (NOS) Center for Operational Oceanographic Products and Services (CO-OPS), are used to support the statutory mandates and all NOAA missions.  The NOAA National Water Level Program (NWLP), the National Current Observation Program (NCOP), and the Physical Oceanographic Real-Time System (PORTS®) are fundamental coastal ocean observing system programs (http://tidesandcurrents.noaa.gov/).  The NWLP is an “end-to-end” system of data collection, quality control, data management, and product delivery.  The NWLP and its methodologies and standard operating procedures for data collection and production of tidal and water level datum products are seen as national standards for certification of information for legal applications and for technology transfer.  The program is seen as a national authority and NOAA accepts responsibility for the accuracy of its products.

The NWLON is the fundamental observing system component of the NWLP.  The NWLON has grown in size since the early 1800s in response to the need for tide and water level information in each of the nation’s ports and for the need to determine tide and water level  datums (Chart Datums : Mean Lower Low Water (MLLW) and Mean High Water (MHW) ) shoreline on a national scale for all U.S. charted waters.  The NWLON provides the long-term continuous measurements of water levels required to maintain national tide and water level datum reference systems.

At present, the NWLON is a coastal observing network of 175 stations nationwide, including the Great Lakes as well as Pacific and Atlantic Ocean Island Territories and Possessions.  The NWLON has expanded geographically and increased in number over time due to national and local needs.  Technological advancements in sensors, data collection, and data communications have enabled near real-time routine automated acquisition and event-driven high rate acquisition over Geostationary Operational Environmental Satellite (GOES).  Because of these advancements, the applications of the NWLON data and products have broadened and the capability of the NWLON has expanded to meet other national needs.  The NWLON is a key observing system component of the NOAA Tsunami Warning System and the NOAA Storm Surge Warning program.

The NWLON is a reference system designed to provide information of the spatial and time-varying nature of tides and water levels.  It provides for the regional description of basic tidal characteristics of time and range of tide and type of tide.  The NWLON provides for the reference harmonic constants used in the NOAA Tide Prediction Tables.  The tide prediction products themselves are part of a national reference system required to meet NOAA missions for navigation products and services.  Because it has the spatial and temporal characteristics of a reference system for tidal datums, it provides control for regional or local observing systems which may have denser local networks.

The NWLON provides information on the spatial and time varying nature of long-term sea level.  Many stations have been in operation for over one century.   A nation-wide picture of relative sea level trends derived from the NWLON stations is routinely reported on and disseminated (NOS, July 2001 and  http://www.co-ops.nos.noaa.gov/sltrends/sltrends.shtml ).  Large spatial gradients in relative mean sea level in regions of significant land movement are not resolved with the NWLON, but the stations provide a reference for regional programs.  The NWLON data also provide information used to understand the response of sea level to the time-varying climate signals of el Nio and la Nia-type oscillations.

The NWLON is configured as a true, long-term observing network.  If one station goes down (i.e., no longer operational), nearby stations can be used for some applications to provide backup sources of information for the particular phenomena of interest (such as control for tidal datums or sea level trends).  These backup stations are not completely redundant, as extrapolation or interpolation will increase the uncertainty in the observations.  There are some stations for which the closest station is too far away to provide network backup.  There are also gaps in NWLON coverage along some areas of the coastline and implementing a denser network nationwide is a long term goal of the program.

2.  NWLON OPERATIONS

The NWLON is managed as a long-term, sustained operational observing system to ensure that the attributes listed above can be maintained.  The NWLON is operated and managed over the long-term with organizational infrastructure in place to operate and maintain the stations and to manage the continuous data collection, data QC, routine product generation, and data and information dissemination.  NOAA maintains a full time Field Operations Division that includes field parties and an instrument shop.  All field work is performed using documented standard operating procedures.  The components of an NWLON station include:

Physical Structure:

- Robust construction of above and below water components to withstand expected environmental extremes, including wind and rain, lightning, waves, currents, extreme high and low waters, vandalism, marine growth, ice and snow.

- Data collection hardware and electronic modules housed in watertight enclosures.

- Yearly preventive maintenance, including underwater maintenance and any corrective or emergency maintenance.

Sensors:

- Use of precise, calibrated or self calibrating, water level measurement sensors that are accurate over the range of water levels to collect extreme lows and storm surge.

- Use of sensors with measurement ranges greater than the expected range of water level.

- Sensors must not have time or elevation drifts or changes in sensor reference zero.

- Implementation of routine calibration checks and swap-out of sensors.

- Use of an independent backup sensor and data logger.

- Configurations used that minimize measurement error sources due to waves, currents and temperature.

- Systems capable of having up to 11 ancillary meteorological and oceanographic sensors configured in addition to the primary and backup sensors.

Vertical Control:

- Station components and sensors are physically mounted such that they will not move except possibly under the most extreme environmental conditions.

- Primary and backup water level sensors are mounted independently to help monitor for vertical movement.

- Differential Second-order, Class I levels are run to connect the sensor leveling point to nearby bench marks on an annual basis to monitor for vertical stability.

- Emergency levels are run if it is known that vertical movement occurred (after storms or earthquakes, for instance).

- If vertical movement is known to have occurred, the data are corrected to ensure a common vertical reference.

Bench Marks:

A minimum local network of 10 bench marks is established in the vicinity of each NWLON station.  Bench marks are spread out such that all will not be destroyed at the same time by construction and development, and are not installed on the same structure such that all will move at the same time.  A primary bench mark is designated and leveled to the sensor zero on an annual basis.  A minimum of five bench marks are leveled to each year, such that all 10 marks are leveled to on a rotating basis every two years.  Vertical stability checks are made and unstable marks are destroyed and replaced by newer bench marks.  Leveling and bench marks installation standards are adhered to in accordance with documented standards.

The NWLON tide and water level datums are typically tied into geodetic datums and the NSRS using level connections and GPS occupations on the benchmarks.

At most stations, a valid tie to at least two marks with NAVD88 orthometric heights (marks with PIDs published in the NGS database) is required on each set of levels, where appropriate marks with NAVD88 heights are available within 1.6 km (1  mi) of the station location.  The tie shall be made in accordance with the procedures stated in section 3.4 of the User's Guide for the Installation of Bench Marks and Leveling Requirements for Water Level Stations, October 1987. For 1st order level runs, a tie with at least three NGS bench marks that have published NAVD 88 elevations is required; for 2nd order and 3rd order level runs, a tie with at least two NGS bench marks that have published NAVD 88 elevations is required.  To perform the NGS tie, start leveling from one NGS mark to the other NGS mark and determine the section elevation difference.  This section elevation difference must be less than the allowable closure tolerance for that section, computed by multiplying a constant K by square root of the distance for the section.  The value of the constant K is equal to 6mm for the 2nd order class 1 levels, and the value of the constant K is equal to 12 mm for the 3rd order levels.  If a tie is made, then connect via levels other bench marks in the leveling network from one of the two NGS bench marks.

If a valid tie is not achieved after leveling to the marks designated in the project instructions for that station, the leveling run shall be extended to other NGS marks, if nearby additional marks are available in the NGS database, until a valid tie is achieved.  If no tie is validated, the levels can only be used by NGS for updating recovery information, but the heights will not be processed.

If the station does not have more than two NAVD88 marks within 1.6 km (1 mi) of the station location, then GPS surveys shall be done to connect tidal datums with geodetic (NAVD88 vertical) datums.   If suitable marks are found in the NGS database, and are farther than 1.6 km (1 mi) but less than 10 km (6 mi) from the tide station, then a GPS tie is required to derive the ellipsoid heights.   The final objective will be to tie the tidal datums at each NWLON station to geodetic datums (NAVD88) through conventional geodetic leveling first, if feasible; if that is not possible, then a relationship shall be determined through the differential GPS techniques.

For NGS Continuously Operating Reference System (CORS) reference bench marks (typically two) that are located within a 1.6 km leveling distance of a water level station, a direct leveling connection shall be made between the CORS reference bench marks and the tidal bench marks in the water level station network every 5 years. The order and class of the leveling run between the CORS reference marks and tidal bench mark shall be the same as that of leveling run for the local level network.   Short term GPS observations will not provide the accuracy required to investigate the long term sea level trends and the correlations with the vertical motion measured at the CORS.

Information about NGS CORS stations can be obtained at http://www.ngs.noaa.gov/CORS/.

The following 8 locations have been identified where the CORS site is located near the tide station.  The distance displayed below is radial distance and may be different from the actual leveling distance from the tide station to the CORS reference marks.

| NWLON Station | Nearby CORS Designation | Approximate Distance (km) |
| --- | --- | --- |
| Eastport ME | EPRT | 0.8 |
| Bar Harbor, ME | BARH | 1.4 |
| Newport, RI | NPRI | 0.5 |
| Sandy Hook, NJ | SHK1 | 0.5 |
| Solomons Island, MD | SOL1 | 0.2 |
| Honolulu, HI | HNLC | 0.0 |
| Hilo, HI | HILO | <1 |
| Kodiak, AK | KODK | <1 |

General Goals for implementing GPS technology in the NWLP.

GPS technology and procedures will be implemented in the operational plan:

(1)	to support the development of a seamless, geocentric reference system for the acquisition, management, and archiving of NOS water level data. This will provide a national and global digital database, which will comply with the minimum geo-spatial metadata standards of the National Spatial Data Infrastructure (NSDI) and connect the NOS water level database to the NGS National Spatial Reference System (NSRS);

(2)	to establish transformation functions between NOS chart datum (MLLW) and the geocentric reference system to support NOS 3-dimensional hydrographic surveys, the implementation of Electronic Chart Display and Information Systems (ECDIS), and the NOS Vertical Datum transformation (V-Datum tool) and tidal datum models.  Integration of GPS procedures into CO-OPS PORTS® operations will support the development of tidally-controlled Digital Elevation Maps and Models for use in programs such as marsh restoration.

(3)	to support water level datum transfers by using GPS derived orthometric heights.

(4)	to monitor crustal motions (horizontal and vertical) to support global climate change investigations.

GPS-derived orthometric heights can be accurately determined and used for water level datum transfers according to (a) the established guidelines for 3-D precise relative positioning to measure ellipsoid heights, (b) properly connecting to several NAVD88 bench marks, and ©) using the latest high-resolution modeled geoid heights for the area of interest.  In many remote locations, the use of GPS-derived orthometric heights for datum transfer will be more efficient (timely) and more cost-effective than the use of conventional differential surveying techniques and may, under certain circumstances, preclude the installation of additional water level stations to establish a datum.

If none of the meteorological sensors (air temperature, barometric pressure, and relative humidity) are available for recording observations, then note any change in the atmospheric conditions on the GPS station/bench mark observation log form under Remarks section.

Data Collection:

The NWLON is managed to collect continuous and valid data series.  Accurate monthly means cannot be computed for a month of data with a break in the water level measurement series in excess of three days.  Even breaks of significantly less than three days will not allow for interpolation during times when strong meteorological conditions are present and in areas with little periodic tidal influence.  Any break in the water level measurement series affects the accuracy of datum computations.  At a critical measurement site where the primary water level measurement data cannot be transmitted or monitored, data from an independent backup sensor is used to fill gaps.

- Data collection is managed by standard configurations of operating system software and application software (firmware) in the Data Collection Platform (DCP) that controls all sensor data collection, storage, and formatting of satellite transmissions and alternative DCP outputs.

- Data are collected continuously, automatically and remotely using hourly GOES transmissions (Libraro, June 1998) to a centralized data management system at NOAA headquarters in Silver Spring for near real-time quality control and dissemination and subsequent downstream data processing and product generation.  Data are also simultaneously collected and reviewed by redundant systems at field party headquarters.

- The DCP includes telephone modems for automatic back-up for data collection and for remote access for running system diagnostic checks and upgrade of DCP software and configurations.

- DCP storage allows for retrieval of data after temporary data transmission failures and for on-site retrieval by field personnel.

- System allows for high rate (every 18-minutes) GOES data transmission after automated or manually set triggers are invoked during storm events or and every 6-minutes for tsunami events.

- Primary power source for the systems is battery-charger systems with solar panels.

- The backup sensor data are collected by an independent DCP isolated from the primary DCP.

Data Quality Control and Data Processing:

The data that come in over hourly GOES transmissions from each station undergo automatic quality control checks .   Flags for these quality control checks are set for each data point and loaded into the Database Management System (DMS).  The data and the flags are reviewed on a 24 X 7 basis by a semi-automated Continuously Operating Real-Time Monitoring System (CORMS) in which CORMS operators review data quality and total system operation using 12-hour shifts.  The CORMS is beginning to use automated case-based and rules-based decision- making tools to assist with reviewing all of the sensors and systems required.  System and data problems are forwarded to appropriate field and headquarters personnel who are on call 24 X 7 to determine and carry out corrective action as required.  All data processing and product generation use documented standard operating procedures.

Data Management:

A robust computer hardware and software environment is maintained and upgraded for the data processing, data analysis, datum computations, product generation, and data dissemination.  A relational DMS is employed that allows for routine and ad hoc queries, and allows for outside web-site interface access using stored procedures.  Six-minute data, hourly heights, high and low waters, daily means and monthly means are produced and verified on a calendar month basis.  All products are independently verified before being accessible to outside users on the web-interface.  The monthly products undergo further data quality assurance at yearly time steps to ensure proper long-term operation.  The DMS also serves as the permanent archival system for all historical data and derived products.  The DMS serves as the source for accepted tidal datums for the nation.  The NWLP requires a substantial data management strategy in which verified data streams are used to compute tidal datums using legally accepted procedures.  The DMS contains the time history of station and sensors configurations, station inspection and repair reports, and leveling and bench mark histories that provide the metadata for the observations.

Data and Product Delivery:

The NWLON is also multipurpose and supports other NOAA missions that are national in scope:

- It is a fundamental component of NOAA’s capability for storm surge monitoring and warning.  The NWLON data are routine data sets to the NOAA Advanced Weather Information Processing System (AWIPS) system.  The NWLON stations also can be automatically put into high-rate satellite dissemination on a user-driven or event-driven trigger.  These data become part of the National Weather Service (NWS) pipeline for marine forecasts.  An increasing percentage of the NWLON stations have meteorological sensors installed.

- It is a fundamental component of NOAA’s capability for tsunami warning.  The NOAA Tsunami Warning Centers have access to high-rate data through the GOES when events are manually or automatically triggered.

- In addition to meteorological sensors, the NWLON stations are capable of adding other sensors for long-term measurements for water conductivity and temperature and for water quality parameters.

A comprehensive CO-OPS web-site is maintained and allows users full access to all data and products on a 24 X 7 basis (http://tidesandcurrents.noaa.gov/.  All raw observed data (6-minute data with quality control flags attached) are automatically available over the web-site after the data collection systems receive each hourly transmission and after they undergo the quality control checks.  Derived data products are made available through the web-site after verification.

Harmonic analyses are routinely performed and accepted sets of harmonic constants used for

tidal prediction are maintained in the database and made available over the web-site.  Tide prediction products based upon the accepted sets of harmonic constituents are also made available “on-the-fly” over the web-site.

Great Lakes and Tidal datums are updated over time and system-wide tidal datum updates to new National Tidal Datum Epochs are made using the archived data and derived products in the data base.  Accepted tidal datums are maintained and can be accessed over the web-site as well.  Tidal datums are computed using documented standard operating procedures.  Published bench mark sheets showing bench mark locations and elevations are prepared and updated and accessible over the web-site.

During storm events and other human-induced events, real-time (6-minute) data are made immediately available to users (http://tidesonline.nos.noaa.gov/ and http://glakesonline.nos.noaa.gov/ .

Real-time water level data in context with other real-time data are accessible for some NWLON stations if they are part of a local PORTS®  (http://tidesandcurrents.noaa.gov/d_ports.html).

APPENDIX 3.  University of Hawaii Sea Level Center Program Description

The University of Hawaii Sea Level Center (UHSLC) collects, processes, and distributes tide gauge measurements from around the world in support of various climate research activities.  Funding for the UHSLC is provided by the Office of Climate Observation (OCO), NOAA.  UHSLC data are used for the evaluation of numerical models, joint analyses with satellite altimeter datasets, the calibration of altimeter data, the production of oceanographic products through the WMO/IOC JCOMM Sea Level Program in the Pacific (SLP-Pac) program, and research on sea level rise and interannual to decadal climate fluctuations.  In support of satellite altimeter calibration and validation and for absolute sea level rise monitoring, the UHSLC and the Pacific GPS Facility maintain co-located GPS systems at select tide gauge stations (GPS@TG).  The UHSLC currently is a designated CLIVAR Data Assembly Center (DAC) and an IOC GLOSS data archive center.  The UHSLC distributes data directly from its own web site and through a dedicated OPeNDAP server.  The data are redistributed by the National Oceanographic Data Center (NODC), the Permanent Service for Mean Sea Level, the Climate Data Portal (CDP) maintained by the Pacific Marine Environmental Laboratory, the National Virtual Ocean Data System (NVODS), the International Pacific Research Center’s GODAE data server, and the NOAA Observing System Architecture (NOSA) web site.

The UHSLC distributes three sea level data sets:

1) The Joint Archive for Sea Level (JASL) data set is designed to be user friendly, scientifically valid, well-documented, and standardized for archiving at international data banks. JASL data are provided internally by the UH Sea Level Network and by over 60 agencies representing over 70 countries.  In the past year, the UHSLC increased its JASL holdings to 10,007 station-years of hourly quality assured data.  The JASL set now includes 5617 station years of data in 264 series at 202 GLOSS sites.

2) The Fast Delivery Database supports various international programs, in particular CLIVAR and GCOS.  The database has been designated by the IOC as a component of the GLOSS program.  The fast delivery data are used extensively by the altimeter community for ongoing assessment and calibration of satellite altimeter datasets.  The fast delivery sea level dataset now includes 141 stations, 113 of which are located at GLOSS sites.

3) Near Real-Time Data (collection + up to a three hour delay, H-3 delay) and daily filtered values (J-2 delay) are provided by the UHSLC in support of GODAE.  Approximately 50 stations currently are available in real-time with plans for ongoing expansion.  When operational, we will distribute this product through our public web site, and make it available in a netCDF format via OPeNDAP server for use in forecast models and for satellite altimeter calibration.

The UHSLC provides monthly maps of the Pacific sea level fields through the JCOMM sponsored SLP-Pac.  UHSLC also produces quarterly updates of an index of the tropical Pacific upper layer volume and annual updates of indices of the ridge-trough system and equatorial currents for the Pacific Ocean.  The analysis includes tide gauge and altimeter sea surface elevation comparisons.

Table A-3-1 Stations that UHSLC brings into the Fast Delivery and Real-time datasets

The GLOSS/CLIVAR (formerly known as the WOCE) fast sea level data is

distributed as hourly, daily, and monthly values.  This project is supported

by the NOAA Climate and Global Change program, and is one of the activities

of the University of Hawaii Sea Level Center.

STATION          LAT    LONG      COUNTRY                    YEARS

POHNPEI          06 59N 158 15E   Fd. St. Micronesia         1985-2004

BETIO            01 22N 172 56E   Kiribati                   1998-2004

BALTRA           00 26S 090 17W   Galapagos Ecuador          1985-2002

NAURU            00 32S 166 54E   Nauru                      1995-2004

MAJURO           07 06N 171 22E   Marshall Islands           2000-2004

MALAKAL          07 20N 134 28E   Belau                      1985-2004

YAP              09 31N 138 08E   Fd. St. Micronesia         1985-2004

HONIARA          09 26S 159 57E   Solomon Islands            1995-2004

RABAUL           04 12S 152 11E   Papau New Guinea           1985-2004

CHRISTMAS        01 59N 157 28W   Kiribati                   1985-2004

KANTON           02 49S 171 43W   Kiribati                   1985-2001

FRENCH FR SHALL  23 52N 166 17W   U.S.A. Hawaii              1985-2004

PAPEETE          17 32S 149 34W   French Polynesia           1985-2004

RIKITEA          23 08S 134 57W   French Polynesia           1985-2004

SUVA             18 08S 178 26E   Fiji                       1998-2004

NOUMEA           22 18S 166 26E   New Caledonia              1985-2004

JUAN FERNANDEZ   33 37S 078 50W   Chile                      1990-1998

EASTER           27 09S 109 27W   Chile                      1985-2004

RAROTONGA        21 12S 159 47W   Cook Islands               1997-2004

PENRHYN          08 59S 158 03W   Cook Islands               1985-2004

FUNAFUTI         08 32S 179 13E   Tuvalu                     2000-2004

SAIPAN           15 14N 145 45E   Mariana Islands            1985-2004

KAPINGAMARANGI   01 06N 154 47E   Fd. St. Micronesia         1985-2004

SANTA CRUZ       00 45S 090 19W   Galapagos Ecuador          1985-2004

NUKU HIVA        08 56S 140 05W   French Polynesia           1985-1998

CABO SAN LUCAS   22 53N 109 55W   Mexico                     1985-2004

SAN FELIX        26 17S 080 08W   Chile                      1992-1997

NUKU'ALOFA       21 08S 175 12W   Tonga                      1990-2004

KODIAK ISLAND    57 44N 152 31W   U.S.A. Alaska              1985-2004

ADAK ISLAND      51 52N 176 38W   U.S.A. Alaska              1985-2004

DUTCH HARBOR     53 54N 166 30W   U.S.A. Alaska              1992-2004

PORT VILA        17 46S 168 18E   Vanuatu                    1993-2004

CHICHIJIMA       27 06N 142 11E   Japan                      1985-2004

MINAMITORISHIMA  24 18N 153 58E   Japan                      2002-2004

MIDWAY ISLAND    28 13N 177 22W   U.S.A. Trust               1985-2004

WAKE ISLAND      19 17N 166 37E   U.S.A. Trust               1985-2004

JOHNSTON ISLAND  16 45N 169 31W   U.S.A. Trust               1985-2004

GUAM             13 26N 144 39E   U.S.A. Trust               1985-2004

KWAJALEIN        08 44N 167 44E   Marshall Island            1985-2004

PAGO PAGO        14 17S 170 41W   U.S.A. Samoa               1985-2002

HONOLULU         21 18N 157 52W   U.S.A. Hawaii              1985-2004

NAWILIWILI       21 58N 159 21W   U.S.A. Hawaii              1985-2004

KAHULUI          20 54N 156 28W   U.S.A. Hawaii              1985-2004

HILO             19 44N 155 04W   U.S.A. Hawaii              1985-2004

CHATHAM ISLAND   43 57S 176 34W   New Zealand                2000-2003

VALPARAISO       33 02S 071 38W   Chile                      1985-2001

ARICA            18 28S 070 20W   Chile                      1985-1999

LOBOS DE AFUERA  06 56S 080 43W   Peru                       1985-1999

QUEPOS           09 24N 084 10W   Costa Rica                 1985-1995

CALDERA          27 04S 070 50W   Chile                      1985-2001

SOCORRO          18 44N 111 01W   Mexico                     1992-1997

LA LIBERTAD      02 12S 080 55W   Ecuador                    1985-2003

TALARA           04 35S 081 17W   Peru                       1992-1996

CALLAO           12 03S 077 09W   Peru                       1985-2004

MOMBASA          04 04S 039 39E   Kenya                      1986-2003

PORT LOUIS       20 09S 057 30E   Mauritius                  1986-2004

DIEGO GARCIA     07 17S 072 24E   United Kingdom             2003-2004

RODRIGUES        19 40S 063 25E   Mauritius                  1986-2004

HULHULE          04 11N 073 32E   Republic of Maldives       1989-2004

GAN              00 41S 073 09E   Republic of Maldives       1987-2004

MASIRAH          20 41N 058 52E   Oman                       1996-2004

SALALAH          16 56N 054 00E   Oman                       1989-2004

HANIMAADHOO      06 46N 073 10E   Maldives                   2003-2004

POINT LA RUE     04 40S 055 32E   Seychelles                 1993-2004

KO TAPHAO NOI    07 50N 098 26E   Thailand                   1985-2003

LAMU             02 16S 040 54E   Kenya                      1995-2004

ZANZIBAR         06 09S 039 11E   Tanzania                   1985-2004

DARWIN           12 28S 130 51E   Australia                  1985-2004

COCOS ISLAND     12 07S 096 54E   Australia                  1985-2004

ESPERANCE        33 52S 121 54E   Australia                  1985-2004

CROZET ISLAND    46 26S 051 52E   France                     1995-2001

ST. PAUL         38 43S 077 32E   France                     2003-2004

KERGUELEN        49 21S 070 13E   France                     1993-2004

RICHARD'S BAY    28 47S 032 06E   South Africa               2003-2004

PONTA DELGADA    37 44N 025 41W   Azores                     1994-2004

SIMON'S BAY      34 11S 018 26E   South Africa               2003-2004

DAKAR            14 40N 017 26W   Senegal                    1994-2003

LOME             06 08N 001 17E   Togo                       1989-1993

SAO TOME         00 21N 006 44E   Sao Tome                   2004-2004

CAPE VERDE       16 45N 022 59W   Cape Verde                 2000-2002

KEY WEST         24 33N 081 49W   U.S.A. Florida             1985-2004

SAN JUAN         18 28N 066 07W   U.S.A. Puerto Rico         1985-2004

NEWPORT          41 30N 071 20W   U.S.A  Rhode Island        1985-2004

SETTLEMENT POINT 26 43N 078 60W   United Kingdom Bahamas     2002-2004

BERMUDA          32 22N 064 42W   United Kingdom             1985-2004

DUCK PIER        36 11N 075 44W   U.S.A. North Carolina      1985-2004

CHARLESTON       32 47N 079 56W   U.S.A. South Carolina      1985-2004

ATLANTIC CITY    39 21N 074 25W   U.S.A. New Jersey          1985-2004

CRISTOBAL        09 21N 079 54W   Panama                     2001-2004

BASQUES          47 34N 059 08W   Canada                     1997-2004

CHURCHILL        58 47N 094 12W   Canada                     1985-2004

HALIFAX          44 40N 063 35W   Canada                     1985-2004

ST-JOHN'S        47 34N 052 43W   Canada                     1993-2004

ILHA FISCAL      22 54S 043 10W   Brazil                     1985-2004

FORTALEZA        03 43S 038 28W   Brazil                     1999-2000

PORT STANLEY     51 42S 057 51W   United Kingdom             2003-2004

ASCENSION        07 54S 014 23W   United Kingdom             1993-2001

ST. HELENA       15 58S 005 42W   United Kingdom             2003-2004

LERWICK          60 09N 001 08W   United Kingdom             1985-2002

NEWLYN           50 06N 005 33W   United Kingdom             1985-2004

STORNOWAY        58 13N 006 23W   United kingdom             1985-2004

BALBOA           08 58N 079 34W   Panama                     1985-2004

KO LAK           11 48N 099 49E   Thailand                   1985-2003

QUARRY BAY       22 18N 114 13E   Hong Kong, PRC             1986-2004

BRISBANE         27 22S 153 10E   Australia                  1985-2004

BUNDABERG        24 50S 152 21E   Australia                  1985-2004

FORT DENISON     33 51S 151 14E   Australia                  1985-2004

TOWNSVILLE       19 15S 146 50E   Australia                  1985-2004

SPRING BAY       42 33S 147 56E   Australia                  1985-2004

ABASHIRI         44 01N 144 17E   Japan                      2001-2004

HAMADA           34 54N 132 04E   Japan                      2001-2004

TOYAMA           36 46N 137 13E   Japan                      2001-2004

KUSHIRO          42 58N 144 23E   Japan                      1985-2004

OFUNATO          39 04N 141 43E   Japan                      1985-2004

MERA             34 55N 139 50E   Japan                      1985-2004

KUSHIMOTO        33 28N 135 47E   Japan                      1985-2004

ABURATSU         31 34N 131 25E   Japan                      1985-2004

NAHA             26 13N 127 40E   Japan                      1985-2004

WAKKANAI         45 24N 141 41E   Japan                      2001-2004

NAGASAKI         32 44N 129 52E   Japan                      1985-2004

HAKODATE         41 47N 140 44E   Japan                      1985-2004

MANZANILLO       19 03N 104 20W   Mexico                     1992-2004

LOMBRUM          02 02S 147 22E   Papua New Guinea           1994-2004

LAUTOKA          17 36S 177 26E   Fiji                       1992-2004

JACKSON          43 59S 168 37E   New Zealand                1999-2004

PRINCE RUPERT    54 19N 130 20W   Canada                     1985-2004

SAN FRANCISCO    37 48N 122 28W   U.S.A. California          1985-2004

CRESCENT CITY    41 45N 124 11W   U.S.A. California          1985-2004

NEAH BAY         48 22N 124 37W   U.S.A. Washington          1985-2004

SITKA            57 03N 135 21W   U.S.A. Alaska              1985-2004

SEWARD           60 07N 149 26W   U.S.A. Alaska              1985-2004

SAN DIEGO        32 43N 117 10W   U.S.A. California          1985-2004

YAKUTAT BAY      59 33N 139 44W   U.S.A. Alaska              1985-2004

KETCHIKAN        55 20N 131 38W   U.S.A. Alaska              1985-2004

SAND POINT       55 20N 160 30W   U.S.A. Alaska              1996-2004

PRUDHOE BAY      70 24N 148 32W   U.S.A. Alaska              1994-2004

SOUTH BEACH      44 38N 124 03W   U.S.A. Oregon              1985-2004

NOME,NORTON SOUND64 30N 165 26W   U.S.A. Alaska              1992-2004

DIEGO RAMIREZ    56 31S 068 43W   Chile                      1993-1998

USHUAIA          54 48S 068 18W   Argentina                  1996-2004

ESPERANZA        63 24S 056 59W   Argentina(Antartica)       2003-2003

TANJONG PAGAR    01 15N 103 51E   Singapore                  1985-2004

PORT NOLLOTH     29 17S 016 51E   South Africa               2004-2004

ROCAS,ATOL DAS   03 51S 033 49W   Brazil                     1999-2000

FORT PULASKI     32 02N 080 54W   U.S.A. Georgia             1985-2004

PENSACOLA        30 24N 087 13W   U.S.A. Florida             1985-2004

GALVESTON(PIER21)29 19N 094 48W   U.S.A. Texas               1985-2004

ANDENES          69 19N 016 09E   Norway                     2001-2004

HONNINGSVARG     70 59N 025 59E   Norway                     2001-2004

MLLOY            61 56N 005 07E   Norway                     2001-2004

RORVIK           64 52N 011 15E   Norway                     2001-2004

TREGDE           58 00N 007 34E   Norway                     2001-2004

VARDO            70 20N 031 06E   Norway                     2001-2004

HADERA           32 28N 034 53E   Israel                     2003-2004

Table A-3-2.  JASL station data

Joint Archive for Sea Level:   Research Quality Data Set

The Joint Archive for Sea Level (JASL), a collaboration between the University of Hawaii Sea Level Center (UHSLC) and the World Data Center-A for

Oceanography, the National Oceanographic Data Center (NODC), and the National

Coastal Data Development Center (NCDDC), continues to acquire, quality

control, manage, and distribute sea level data as initiated by the Tropical

Ocean Global Atmosphere (TOGA) Program, which ended in 1994.  The TOGA ocean

monitoring networks were primarily in the tropics.  Since the end of TOGA, the JASL has slowly begun to absorb sea level sites in oceanographically strategic locations beyond the tropics.  The JASL is now an official Global Sea Level Observing System (GLOSS) data center.  The JASL Research Quality Data Set (RQDS) is the largest global collection of quality-controlled hourly sea level.  Efforts are underway to acquire new sites and uncover historic recordsas available.

The JASL receives hourly data from regional and national sea level networks.   The data are inspected and obvious errors such as data spikes and time shifts are corrected.  Gaps less than 25 hours are interpolated. Reference level problems are referred back to the originator.  If the originators can not resolve the reference level shift, comparisons with neighboring sites or

examination of the hourly residuals may warrant an adjustment.  Descriptive station information and quality assessments are prepared.  The objective is to assemble a scientifically valid, well-documented archive of hourly, daily, and monthly sea level values in standardized formats.  These data are annually submitted to the World Data Center-A for Oceanography (WDCA) and the monthly values are provided to the Permanent Service for Mean Sea Level.

GLOBAL

# Series: 525

# Site-years: 10,007

GENERAL INFORMATION FOR DESIRED STATIONS: Pacific Ocean

# Series = 283

# Site-years = 5958

Notes on columns:

CI: Completeness index or percentage of data span without missing data.

QC-YEARS: years which have received quality control.

GLOS STATION           COUNTRY           LAT    LONG    QC-YEARS   CI CONTRIBUTOR

115  Pohnpei-A         Fd St Micronesia  06-59N 158-14E 1969-1971 100 Scripps Inst. Ocean

115  Pohnpei-B         Fd St Micronesia  06-59N 158-15E 1974-2003  98 UH Sea Level Center

113  Tarawa-A,Betio    Rep. of Kiribati  01-22N 172-56E 1974-1983  78 UH Sea Level Center

113  Tarawa-B,Bairiki  Rep. of Kiribati  01-20N 173-01E 1983-1988  98 UH Sea Level Center

113  Tarawa-C,Betio    Rep. of Kiribati  01-22N 172-56E 1988-1997 100 UH Sea Level Center

113  Tarawa-D,Betio    Rep. of Kiribati  01-22N 172-56E 1992-2003  91 Nat. Tidal Facility

169  Baltra-A          Ecuador           00-26S 090-17W 1968-1977  93 National Ocean Service

169  Baltra-B          Ecuador           00-26S 090-17W 1985-2002  98 UH Sea Level Center

114  Nauru-A           Rep. of Nauru     00-32S 166-54E 1974-1995  95 UH Sea Level Center

114  Nauru-B           Rep. of Nauru     00-32S 166-55E 1993-2003  90 Nat. Tidal Facility

112  Majuro-A          Rep. Marshall I.  07-06N 171-22E 1968-1999  92 UH Sea Level Center

112  Majuro-B          Rep. Marshall I.  07-07N 171-22E 1993-2003  97 Nat. Tidal Facility

xxx  Enewetok-A        Rep. Marshall I.  11-26N 162-23E 1951-1971  98 Scripps Inst. Ocean.

xxx  Enewetok-B        Rep. Marshall I.  11-26N 162-23E 1974-1979  94 UH Sea Level Center

120  Malakal-A         Rep. of Belau     07-20N 134-29E 1929-1937  98 Japan Ocean. Data Cen.

120  Malakal-B         Rep. of Belau     07-20N 134-28E 1969-2003  95 UH Sea Level Center

119  Yap-A             Fd St Micronesia  09-31N 138-08E 1951-1952 100 Scripps Inst. Ocean.

119  Yap-B             Fd St Micronesia  09-31N 138-08E 1969-2003  93 UH Sea Level Center

066  Honiara-A         Solomon Islands   09-26S 159-57E 1974-1995  98 UH Sea Level Center

066  Honiara-B         Solomon Islands   09-25S 159-57E 1994-2003  97 Nat. Tidal Facility

065  Rabaul            Papua New Guinea  04-12S 152-11E 1966-1997  85 UH Sea Level Center

146  Christmas-A       Rep. of Kiribati  01-59N 157-29W 1955-1972  89 Scripps Inst. Ocean.

146  Christmas-B       Rep. of Kiribati  01-59N 157-28W 1974-2003  96 UH Sea Level Center

xxx  Fanning-A         Rep. of Kiribati  03-54N 159-23W 1957-1958  88 Scripps Inst. Ocean.

xxx  Fanning-B         Rep. of Kiribati  03-54N 159-23W 1972-1987  95 UH Sea Level Center

xxx  Fanning-C         Rep. of Kiribati  03-51N 159-22W 1988-1990  78 UH Sea Level Center

145  Kanton-A          Rep. of Kiribati  02-49S 171-43W 1949-1967 100 Scripps Inst. Ocean.

145  Kanton-B          Rep. of Kiribati  02-49S 171-43W 1972-2001  93 UH Sea Level Center

107  French Frigate S  USA               23-52N 166-17W 1974-2001  97 UH Sea Level Center

140  Papeete-A         French Polynesia  17-32S 149-34W 1969-1975  91 UH Sea Level Center

140  Papeete-B         French Polynesia  17-32S 149-34W 1975-2000  99 National Ocean Service

138  Rikitea           French Polynesia  23-08S 134-57W 1969-2003  92 UH Sea Level Center

xxx  Hiva Oa           French Polynesia  09-49S 139-02W 1977-1980  75 UH Sea Level Center

122  Suva-A            Fiji              18-08S 178-26E 1972-1997  91 National Ocean Service

122  Suva-B            Fiji              18-08S 178-26E 1998-2003  99 Nat. Tidal Facility

123  Noumea            France            22-18S 166-26E 1967-2003  99 UH Sea Level Center

176  Juan Fernandez-A  Chile             33-37S 078-50W 1977-1984  67 UH Sea Level Center

176  Juan Fernandez-B  Chile             33-37S 078-50W 1985-2002  89 SHOA

137  Easter-A          Chile             27-09S 109-27W 1957-1958  97 SHOA

137  Easter-B          Chile             27-09S 109-27W 1962-1963 100 SHOA

137  Easter-C          Chile             27-09S 109-27W 1970-2002  83 SHOA

139  Rarotonga-A       Cook Islands      21-12S 159-47W 1977-1997  98 UH Sea Level Center

139  Rarotonga-B       Cook Islands      21-12S 159-47W 1993-2003  99 Nat. Tidal Facility

143  Penrhyn           Cook Islands      08-59S 158-03W 1977-2001  95 UH Sea Level Center

121  Funafuti-A        Tuvalu            08-32S 179-12E 1977-1999  97 UH Sea Level Center

121  Funafuti-B        Tuvalu            08-30S 179-13E 1993-2003  96 Nat. Tidal Facility

xxx  Honolulu,Kewalo   USA               21-18N 157-52W 1978-1986  96 UH Sea Level Center

xxx  Honolulu,Pier 45  USA               21-19N 157-53W 1985-1988 100 UH Sea Level Center

118  Saipan            N. Mariana Is.    15-14N 145-45E 1978-2003  93 UH Sea Level Center

117  Kapingamarangi    Fd St Micronesia  01-06N 154-47E 1978-2001  92 UH Sea Level Center

xxx  Santa Cruz        Ecuador           00-45S 090-19W 1978-2003  95 UH Sea Level Center

142  Nuku Hiva         French Polynesia  08-56S 140-05W 1982-1997  70 UH Sea Level Center

069  Bitung            Indonesia         01-26N 125-12E 1986-1990  94 BAKOSURTANAL

161  Cabo San Lucas    Mexico            22-53N 109-55W 1973-2003  81 CICESE

177  San Felix         Chile             26-17S 080-08W 1987-2002  79 SHOA

160  Guadalupe         Mexico            28-53N 118-18W 1977-1985  75 CICESE

xxx  Nuku'alofa        Tonga             21-08S 175-11W 1990-2003  97 Nat. Tidal Facility

xxx  Kodiak,Alaska     USA               57-44N 152-31W 1975-2003  81 National Ocean Service

302  Adak,Alaska       USA               51-52N 176-38W 1950-2003  92 National Ocean Service

102  Dutch Harbor-A,AK USA               53-53N 166-32W 1950-1955 100 National Ocean Service

102  Dutch Harbor-B,AK USA               53-53N 166-32W 1992-2003 100 National Ocean Service

xxx  Palmyra           USA Trust         05-53N 162-05W 1947-1949  95 National Ocean Service

xxx  Port Vila-A       Vanuatu           17-44S 168-19E 1977-1982  87 unconfirmed

xxx  Port Vila-B       Vanuatu           17-46S 168-18E 1993-2003  92 Nat. Tidal Facility

103  Chichijima        Japan             27-06N 142-11E 1975-2002 100 Japan Meteor. Agency

xxx  Anewa Bay         Papua New Guinea  06-11S 155-53E 1968-1977  85 UH Sea Level Center

xxx  Minamitorishima   Japan             24-18N 153-59E 1997-2002  90 Japan Meteor. Agency

106  Midway            USA Trust         28-13N 177-22W 1947-2003  93 National Ocean Service

105  Wake              USA Trust         19-17N 166-37E 1950-2003  93 National Ocean Service

109  Johnston          USA Trust         16-44N 169-32W 1947-2003  95 National Ocean Service

149  Guam              USA Trust         13-26N 144-39E 1948-2003  92 National Ocean Service

116  Truk              Fd St Micronesia  07-27N 151-51E 1963-1991  89 National Ocean Service

111  Kwajalein         Rep. Marshall I.  08-44N 167-44E 1946-2003  98 National Ocean Service

144  Pago Pago         USA Trust         14-17S 170-41W 1948-2003  95 National Ocean Service

108  Honolulu-A        USA               21-18N 157-52W 1877-1892  32 National Ocean Service

108  Honolulu-B        USA               21-18N 157-52W 1905-2003  98 UH Sea Level Center

xxx  Nawiliwili        USA               21-58N 159-21W 1954-2003  99 National Ocean Service

xxx  Kahului           USA               20-54N 156-28W 1950-2003  92 National Ocean Service

287  Hilo              USA               19-44N 155-04W 1927-2003  81 National Ocean Service

xxx  Mokuoloe          USA               21-26N 157-48W 1957-2003  78 National Ocean Service

124  Norfolk Island-A  Australia         29-04S 167-57E 1985-1986  98 CSIRO

124  Norfolk Island-B  Australia         29-04S 167-56E 1994-1999 100 CSIRO

xxx  Wewak             Papua New Guinea  03-34S 143-38E 1984-1994  82 CSIRO

xxx  Port Moresby      Papua New Guinea  09-29S 147-08E 1984-1993  98 CSIRO

xxx  Manus             Papua New Guinea  02-01S 147-16E 1984-1994  73 CSIRO

xxx  Madang            Papua New Guinea  05-12S 145-48E 1984-1998  81 CSIRO

xxx  Lae               Papua New Guinea  06-44S 146-59E 1984-1997  83 CSIRO

xxx  Kavieng           Papua New Guinea  02-35S 150-48E 1984-1994  95 CSIRO

063  Alotau            Papua New Guinea  10-10S 150-27E 1984-1995  62 CSIRO

127  Auckland          New Zealand       36-51S 174-46E 1984-1988 100 Royal New Zealand Navy

101  Wellington        New Zealand       41-17S 174-47E 1984-1990  91 Royal New Zealand Navy

129  Bluff             New Zealand       46-36S 168-21E 1984-1988  88 Royal New Zealand Navy

xxx  Tauranga          New Zealand       37-39S 176-11E 1984-1985  99 Royal New Zealand Navy

xxx  Westport          New Zealand       41-44S 171-36E 1984-1985 100 Royal New Zealand Navy

xxx  Wanganui          New Zealand       39-57S 174-59E 1984-1985  97 Royal New Zealand Navy

xxx  Taranaki          New Zealand       39-03S 174-02E 1984-1985  79 Royal New Zealand Navy

xxx  Port Nelson       New Zealand       41-16S 173-16E 1984-1985  97 Royal New Zealand Navy

xxx  Gisborne          New Zealand       38-41S 178-02E 1984-1985  98 Royal New Zealand Navy

128  Chatham           New Zealand       43-57S 176-34E 2001-2001  30 UH Sea Level Center

174  Antofagasta       Chile             23-39S 070-24W 1945-2002  93 SHOA

175  Valparaiso        Chile             33-02S 071-38W 1944-2002  84 SHOA

182  Acajutla          El Salvador       13-35N 089-50W 1971-2001  87 Inst. Geograf. Nacional

xxx  Arica             Chile             18-28S 070-20W 1982-1998  98 SHOA

xxx  Lobos de Afuera   Peru              06-56S 080-43W 1982-2001  97 DHNM

170  Buenaventura      Colombia          03-54N 077-06W 1953-2000  93 IDEAM

xxx  La Union          El Salvador       13-20N 087-49W 1954-1980  77 National Ocean Service

167  Quepos            Costa Rica        09-24N 084-10W 1961-1994  83 SERMAR

xxx  Caldera           Chile             27-04S 070-50W 1980-1998  97 SHOA

xxx  Manta             Ecuador           00-57S 080-44W 1979-1981 100 INOCAR

162  Socorro           Mexico            18-44N 111-01W 1957-1959  81 CICESE

172  La Libertad       Ecuador           02-12S 080-55W 1949-2001  97 INOCAR

xxx  Talara-A          Peru              04-35S 081-17W 1950-1965  92 National Ocean Service

xxx  Talara-B          Peru              04-35S 081-17W 1988-2001  74 DHNM

173  Callao-A          Peru              12-03S 077-09W 1950-1965  98 National Ocean Service

173  Callao-B          Peru              12-03S 077-09W 1970-2002 100 DHNM

xxx  Matarani-A        Peru              17-00S 072-07W 1954-1964  98 National Ocean Service

xxx  Matarani-B        Peru              17-00S 072-07W 1992-2001  79 DHNM

xxx  San Juan          Peru              15-22S 075-12W 1978-2001  79 DHNM

xxx  Naos-A            Panama            08-55N 079-32W 1961-1965  99 Scripps Inst. Ocean.

xxx  Naos-B            Panama            08-55N 079-32W 1991-1997  84 National Ocean Service

xxx  Puerto Quetzal-A  Guatemala         13-55N 090-47W 1983-1984  90 UH Sea Level Center

xxx  Puerto Quetzal-B  Guatemala         13-55N 090-47W 1992-1995  77 UH Sea Level Center

168  Balboa            Panama            08-58N 079-34W 1907-1997  98 Panama Canal Commission

171  Tumaco            Colombia          01-50N 078-44W 1951-2000  86 IDEAM

xxx  Pto. Armuelles-A  Panama            08-16N 082-52W 1955-1968  95 Inst. Geograf. Nac.

xxx  Pto. Armuelles-B  Panama            08-16N 082-52W 1983-1998  94 Inst. Geograf. Nac.

xxx  Cedros Island     Mexico            28-06N 115-11W 1976-1989  75 CICESE

xxx  San Felipe        Mexico            31-01N 114-49W 1982-1986  52 UNAM

xxx  San Quintin       Mexico            30-29N 115-59W 1977-1990  97 CICESE

xxx  Bahia Los Angeles Mexico            28-58N 113-33W 1973-1994  74 CICESE

xxx  Catalina-A        USA               33-27N 118-29W 1978-1979  96 Scripps Inst. Ocean.

xxx  Catalina-B        USA               33-27N 118-29W 1980-1988  86 Scripps Inst. Ocean.

267  Acapulco          Mexico            16-50N 099-55W 1952-1995  91 UNAM

xxx  Ensenada          Mexico            31-51N 116-38W 1956-1991  84 UNAM

xxx  Puerto Madero     Mexico            14-43N 092-26W 1986-1988  99 UNAM

xxx  Loreto            Mexico            26-01N 111-22W 1975-1988  73 CICESE

293  Cendering         Malaysia          05-16N 103-11E 1984-2002  99 Dept. Survey/Mapping

xxx  Johor Baharu      Malaysia          01-28N 103-48E 1983-2002  95 Dept. Survey/Mapping

xxx  Kuantan           Malaysia          03-59N 103-26E 1983-2002  99 Dept. Survey/Mapping

xxx  Tioman            Malaysia          02-48N 104-08E 1985-2002  97 Dept. Survey/Mapping

xxx  Sedili            Malaysia          01-56N 104-07E 1986-2002  98 Dept. Survey/Mapping

xxx  Kukup             Malaysia          01-20N 103-27E 1985-2002  98 Dept. Survey/Mapping

xxx  Geting            Malaysia          06-14N 102-06E 1986-2002  99 Dept. Survey/Mapping

044  Keppel Harbour    Singapore         01-16N 103-49E 1981-1990  99 Port Singapore Auth.

039  Ko Lak            Thailand          11-48N 099-49E 1985-2002  96 Naval Hydro. Dept.

077  Hong Kong-A       China             22-18N 114-12E 1962-1985  97 Hong Kong Observatory

077  Hong Kong-B       China             22-18N 114-13E 1986-2003  99 Hong Kong Observatory

058  Brisbane          Australia         27-22S 153-10E 1984-2003  97 Nat. Tidal Facility

059  Bundaberg         Australia         24-50S 152-21E 1984-2003  98 Nat. Tidal Facility

057  Fort Denison      Australia         33-51S 151-14E 1965-2003  94 Nat. Tidal Facility

060  Townsville        Australia         19-16S 146-50E 1984-2002  99 Nat. Tidal Facility

056  Spring Bay        Australia         42-33S 147-56E 1985-2003  95 Nat. Tidal Facility

061  Booby Island      Australia         10-36S 141-55E 1988-1999  88 Nat. Tidal Facility

044  Victoria Dock     Singapore         01-16N 103-49E 1972-1981  95 Port Singapore Auth.

xxx  Macau             Portugal          22-10N 113-33E 1978-1985  80 Inst. Hidro. Marinha

xxx  Hobart            Australia         42-53S 147-20E 1985-1999  83 Nat. Tidal Facility

xxx  Kaohsiung         Rep. of China     22-37N 120-18E 1980-1999  98 Central Weather Bureau

xxx  Keelung           Rep. of China     25-09N 121-45E 1980-1999  93 Central Weather Bureau

327  Abashiri          Japan             44-01N 144-17E 1968-2002  97 Japan Meteor. Agency

326  Hamada            Japan             34-54N 132-04E 1984-2002  95 Japan Meteor. Agency

325  Toyama            Japan             36-46N 137-13E 1967-2002  98 Japan Meteor. Agency

089  Kushiro           Japan             42-58N 144-23E 1963-2002  97 Japan Meteor. Agency

087  Ofunato           Japan             39-01N 141-45E 1965-2002 100 Japan Meteor. Agency

086  Mera              Japan             34-55N 139-50E 1965-2002  93 Japan Meteor. Agency

085  Kushimoto         Japan             33-28N 135-47E 1961-2002  97 Japan Meteor. Agency

082  Aburatsu          Japan             31-34N 131-25E 1961-2002 100 Japan Meteor. Agency

081  Naha              Japan             26-13N 127-40E 1966-2002 100 Japan Meteor. Agency

xxx  Maisaka           Japan             34-41N 137-37E 1968-2002  96 Japan Meteor. Agency

xxx  Miyakejima        Japan             34-04N 139-29E 1965-2001  99 Japan Ocean. Data Cen.

xxx  Hosojima          Japan             32-25N 131-41E 1933-1975  86 Japan Ocean. Data Cen.

xxx  Naze              Japan             28-23N 129-30E 1961-2003  94 Japan Ocean. Data Cen.

324  Wakkanai          Japan             45-25N 141-41E 1967-2002  99 Japan Meteor. Agency

083  Nagasaki          Japan             32-44N 129-52E 1985-2002 100 Japan Meteor. Agency

xxx  Nishinoomote      Japan             30-44N 130-60E 1965-2003  98 Japan Meteor. Agency

088  Hakodate          Japan             41-47N 140-44E 1964-2002  93 Japan Meteor. Agency

xxx  Ishigaki          Japan             24-20N 124-09E 1969-2002 100 Japan Meteor. Agency

073  Manila            Philippines       14-35N 120-58E 1984-2002  96 Ocean. Surveys Div.

072  Legaspi           Philippines       13-09N 123-45E 1984-2002  91 Ocean. Surveys Div.

071  Davao             Philippines       07-05N 125-38E 1984-1997  81 Ocean. Surveys Div.

070  Jolo              Philippines       06-04N 121-00E 1984-1995  86 Ocean. Surveys Div.

xxx  Hachinohe         Japan             40-32N 141-32E 1980-2002 100 Japan Meteor. Agency

247  Xiamen            China             24-27N 118-04E 1954-1997 100 PRC NODC

xxx  Cebu              Philippines       10-18N 123-55E 1998-2002  93 Ocean. Surveys Div.

xxx  Puerto Princesa   Philippines       09-45N 118-44E 1998-2002  84 Ocean. Surveys Div.

xxx  Tawau             Malaysia          04-14N 117-53E 1987-2002  94 Dept. Survey/Mapping

xxx  Kota Kinabalu     Malaysia          05-59N 116-04E 1987-2002  92 Dept. Survey/Mapping

xxx  Bintulu           Malaysia          03-13N 113-04E 1992-2002  85 Dept. Survey/Mapping

xxx  Miri              Malaysia          04-24N 113-58E 1992-1998  91 Dept. Survey/Mapping

xxx  Sandakan          Malaysia          05-49N 118-04E 1993-2002  96 Dept. Survey/Mapping

165  Clipperton-A      France            10-17N 109-13W 1985-1985  47 NOAA/PMEL

165  Clipperton-B      France            10-17N 109-13W 1986-1988 100 NOAA/PMEL

xxx  Puerto Vallarta   Mexico            20-37N 105-15W 1973-1991  40 UNAM

xxx  Salina Cruz       Mexico            16-10N 095-12W 1952-1991  81 UNAM

163  Manzanillo-A      Mexico            19-03N 104-20W 1953-1982  95 UNAM

163  Manzanillo-B      Mexico            19-03N 104-20W 1992-2001  74 National Ocean Service

xxx  Puntarenas        Costa Rica        09-58N 084-50W 1970-1980  71 SERMAR

xxx  Guaymas           Mexico            27-56N 110-54W 1953-1986  81 UNAM

xxx  Marsden Point     New Zealand       35-50S 174-30E 1984-1985  99 Royal New Zealand Navy

148  Lord Howe-A       Australia         31-31S 159-04E 1958-1967  80 Scripps Inst. Ocean.

148  Lord Howe-B       Australia         31-31S 159-04E 1991-1994  99 Nat. Tidal Facility

xxx  Lombrum           Papua New Guinea  02-02S 147-23E 1994-2003  90 Nat. Tidal Facility

xxx  Apia-A            Western Samoa     13-49S 171-45W 1954-1971  88 Scripps Inst. Ocean.

xxx  Apia-B            Western Samoa     13-49S 171-45W 1993-2003  98 Nat. Tidal Facility

xxx  Lautoka           Fiji              17-36S 177-26E 1992-2003  99 Nat. Tidal Facility

xxx  Lungsurannaga     Indonesia         02-06N 117-45E 1943-1944  95 Japan Ocean. Data Cen.

xxx  Balikpapan        Indonesia         01-16S 116-48E 1942-1943 100 Japan Ocean. Data Cen.

xxx  Bajor             Indonesia         00-41S 117-25E 1943-1944  97 Japan Ocean. Data Cen.

155  Prince Rupert-A   Canada            54-19N 130-20W 1910-1918  79 MEDS

155  Prince Rupert-B   Canada            54-19N 130-20W 1963-1999  99 MEDS

156  Tofino            Canada            49-09N 125-55W 1963-1999  94 MEDS

xxx  Victoria,BC       Canada            48-25N 123-22W 1909-1964  98 MEDS

303  Massacre Bay,AK   USA               52-50N 173-12E 1943-1966  88 National Ocean Service

158  San Francisco,CA  USA               37-48N 122-28W 1901-2003 100 National Ocean Service

xxx  Kawaihae,HI       USA               20-02N 155-50W 1989-2003  87 National Ocean Service

xxx  Port Allen,HI     USA               21-54N 159-36W 1989-1997  98 National Ocean Service

xxx  Monterey,CA       USA               36-36N 121-53W 1973-2003  99 National Ocean Service

xxx  Crescent City,CA  USA               41-45N 124-11W 1933-2003  90 National Ocean Service

xxx  Port Orford,OR    USA               42-44N 124-30W 1996-2003  59 National Ocean Service

xxx  Neah Bay,WA       USA               48-22N 124-37W 1934-2003  97 National Ocean Service

154  Sitka-A,AK        USA               57-03N 135-21W 1950-2003  92 National Ocean Service

150  Seward-A,AK       USA               60-07N 149-26W 1925-1932  98 National Ocean Service

150  Seward-B,AK       USA               60-07N 149-26W 1944-1949  77 National Ocean Service

150  Seward-C,AK       USA               60-07N 149-26W 1967-2003  86 National Ocean Service

xxx  Seldovia,AK       USA               59-26N 151-43W 1979-2003 100 National Ocean Service

xxx  Valdez,AK         USA               61-08N 146-22W 1996-2003 100 National Ocean Service

xxx  Willapa Bay,WA    USA               46-43N 123-58W 1996-2003 100 National Ocean Service

xxx  Port San Luis,CA  USA               35-11N 120-46W 1983-2003  85 National Ocean Service

xxx  Los Angeles,CA    USA               33-43N 118-16W 1923-2001  99 National Ocean Service

159  San Diego,CA      USA               32-43N 117-10W 1906-2003  97 National Ocean Service

xxx  Yakutat,AK        USA               59-33N 139-44W 1961-2003  91 National Ocean Service

xxx  Ketchikan,AK      USA               55-20N 131-38W 1918-2003  73 National Ocean Service

xxx  Astoria,OR        USA               46-13N 123-46W 1925-2003  97 National Ocean Service

xxx  Arena Cove,CA     USA               38-55N 123-43W 1996-2003 100 National Ocean Service

100  Sand Point,AK     USA               55-20N 160-30W 1996-2001 100 National Ocean Service

xxx  Charleston,OR     USA               43-21N 124-19W 1978-2003  98 National Ocean Service

xxx  Humboldt Bay,CA   USA               40-46N 124-13W 1993-2003 100 National Ocean Service

xxx  Santa Barbara,CA  USA               34-25N 119-41W 1996-1998  98 National Ocean Service

xxx  Santa Monica,CA   USA               34-01N 118-30W 1996-2003  96 National Ocean Service

151  Prudhoe Bay,AK    USA               70-24N 148-32W 1993-2003 100 National Ocean Service

xxx  Cordova-A,AK      USA               60-34N 145-45W 1949-1953  94 National Ocean Service

xxx  Cordova-B,AK      USA               60-34N 145-45W 1964-2003  84 National Ocean Service

xxx  Matavai           French Polynesia  17-31S 149-31W 1958-1967  65 Scripps Inst. Ocean.

157  South Beach,OR    USA               44-38N 124-03W 1967-2003  99 National Ocean Service

xxx  Harvest Oil P.,CA USA               34-28N 120-40W 1995-1999  20 National Ocean Service

074  Nome, AK          USA               64-30N 165-26W 1992-2001  68 National Ocean Service

180  Diego Ramirez     Chile             56-31S 068-43W 1991-1997  95 SHOA

079  Dalian-A          China             38-56N 121-40E 1975-1990  98 PRC NODC

079  Laohutan-A        China             38-52N 121-41E 1991-1997 100 PRC NODC

094  Kanmen-A          China             28-05N 121-17E 1975-1997 100 PRC NODC

283  Lusi-A            China             32-08N 121-37E 1975-1996  98 PRC NODC

078  Zhapo-A           China             21-35N 111-50E 1975-1997 100 PRC NODC

xxx  Beihai            China             21-29N 109-05E 1975-1997 100 PRC NODC

xxx  Dongfang          China             19-06N 108-37E 1975-1997 100 PRC NODC

xxx  Haikou            China             20-01N 110-17E 1976-1997 100 PRC NODC

xxx  Lianyungang       China             34-45N 119-25E 1975-1997 100 PRC NODC

xxx  Shanwei           China             22-45N 115-21E 1975-1997  98 PRC NODC

xxx  Shijiusuo         China             35-23N 119-33E 1975-1997 100 PRC NODC

xxx  Hon Dau-A         Vietnam           20-40N 106-49E 1960-1960 100 Mar. Hydromet. Center

xxx  Hon Dau-B         Vietnam           20-40N 106-49E 1995-1995  75 TEDIPORT

xxx  Vung Ang          Vietnam           18-05N 106-17E 1996-1997 100 TEDIPORT

xxx  Vung Tau          Vietnam           10-20N 107-04E 1992-1992 100 TEDIPORT

xxx  Champerico        Guatemala         14-18N 091-55W 1974-1975  98 Oregon State Univerity

xxx  La Paz            Mexico            24-10N 110-21W 1952-1983  71 UNAM

xxx  Puerto Angel      Mexico            15-39N 096-30W 1962-1984  74 UNAM

xxx  Mazatlan          Mexico            23-12N 106-25W 1953-1975  97 UNAM

xxx  San Carlos        Mexico            24-47N 112-07W 1968-1983  51 UNAM

xxx  San Jose          Guatemala         13-55N 090-50W 1955-1975  93 Oregon State Univerity

xxx  Topolobampo       Mexico            25-36N 109-03W 1956-1974  94 UNAM

xxx  Yavaros           Mexico            26-42N 109-31W 1970-1973  85 UNAM

xxx  Paita-A           Peru              05-05S 081-10W 1981-1984 100 National Ocean Service

xxx  Paita-B           Peru              05-05S 081-10W 1988-2001  90 DHNM

xxx  Corinto           Nicaragua         12-17N 087-07W 1967-1967  99 National Ocean Service

xxx  San Martin-A      Argentina         68-08S 067-06W 1995-1995   8 Alfred Wegener Inst.

xxx  San Martin-B      Argentina         68-08S 067-06W 1998-1998   5 Alfred Wegener Inst.

xxx  San Martin-C      Argentina         68-08S 067-06W 1998-1999 100 Alfred Wegener Inst.

xxx  Dallmann-A        Argentina         62-14S 058-41W 1996-1997  99 Alfred Wegener Inst.

xxx  Dallmann-B        Argentina         62-14S 058-41W 1997-1997  69 Alfred Wegener Inst.

xxx  Dallmann-C        Argentina         62-14S 058-41W 1998-1999 100 Alfred Wegener Inst.

xxx  Pisco-A           Peru              13-25S 076-08W 1985-1990  67 DHNM

xxx  Pisco-B           Peru              13-25S 076-08W 1991-2001  82 DHNM

178  Puerto Montt      Chile             41-29S 072-58W 1980-2002  93 SHOA

xxx  Tinian            N. Mariana Is.    14-58N 145-37E 1991-1997  93 USGS

044  Tanjong Pagar     Singapore         01-16N 103-51E 1988-2001  93 Port Singapore Auth.

GENERAL INFORMATION FOR DESIRED STATIONS: Indian Ocean

# Series: 71

# Site-years: 737

column notes:

CI: Completeness index or percentage of data span without missing data.

QC-YEARS: years which have received quality control.

GLOS STATION           COUNTRY           LAT    LONG    QC-YEARS   CI  CONTRIBUTOR

008  Mombasa           Kenya             04-04S 039-39E 1986-2001  78 UH Sea Level Center

xxx  Dar Es Salaam     Tanzania          06-49S 039-17E 1986-1990  87 UH Sea Level Center

018  Port Louis-A      Mauritius         20-09S 057-29E 1942-1947  90 Inst. Ocean. Sciences

018  Port Louis-B      Mauritius         20-09S 057-29E 1964-1965  86 Inst. Ocean. Sciences

018  Port Louis-C      Mauritius         20-09S 057-30E 1986-2001  99 UH Sea Level Center

026  Diego Garcia-B    United Kingdom    07-14S 072-26E 1969-1969  41 Scripps Inst. Ocean.

026  Diego Garcia-C    United Kingdom    07-17S 072-24E 1988-2000  80 UH Sea Level Center

019  Rodrigues         Mauritius         19-40S 063-25E 1986-2001  96 UH Sea Level Center

xxx  Praslin           Seychelles        04-21S 055-46E 1987-1989  89 UH Sea Level Center

045  Padang            Indonesia         01-00S 100-22E 1986-1990  86 BAKOSURTANAL

028  Male-A            Rep. of Maldives  04-11N 073-31E 1988-1989 100 Lanka Hydraulic Inst.

028  Male-B,Hulule     Rep. of Maldives  04-11N 073-32E 1989-2001  90 UH Sea Level Center

027  Gan               Rep. of Maldives  00-41S 073-09E 1987-2001  87 UH Sea Level Center

xxx  Muscat            Oman              23-38N 058-34E 1987-1993  77 UH Sea Level Center

273  Port Victoria-A   Seychelles        04-37S 055-28E 1977-1982  84 Inst. Ocean. Sciences

273  Port Victoria-B   Seychelles        04-37S 055-28E 1986-1992  96 UH Sea Level Center

xxx  Masirah           Oman              20-41N 058-52E 1996-2003  94 UH Sea Level Center

004  Salalah           Oman              16-56N 054-00E 1989-2003  87 UH Sea Level Center

033  Colombo-A         Sri Lanka         06-56N 079-51E 1953-1965  94 Nat. Aquatic Resources

033  Colombo-B         Sri Lanka         06-57N 079-51E 1989-1992  96 UH Sea Level Center

xxx  Hanimaadhoo       Rep. of Maldives  06-46N 073-10E 1991-2002  98 UH Sea Level Center

273  Pt. La Rue        Seychelles        04-40S 055-32E 1993-2001  98 UH Sea Level Center

xxx  Hiron Point       Bangladesh        21-47N 089-28E 1977-2000  99 BIWTA

xxx  Khal #10          Bangladesh        22-16N 091-49E 1983-1992  62 BIWTA

xxx  Cox's Bazaar      Bangladesh        21-27N 091-50E 1983-2000  98 BIWTA

xxx  Teknaf            Bangladesh        20-53N 092-18E 1983-1988  59 BIWTA

036  Charchanga        Bangladesh        22-13N 091-03E 1980-2000  97 BIWTA

xxx  Khepupara         Bangladesh        21-50N 089-50E 1987-2000  96 BIWTA

xxx  Kelang            Malaysia          03-03N 101-22E 1983-2002  99 Dept. Survey/Mapping

xxx  Keling            Malaysia          02-13N 102-09E 1984-2002  99 Dept. Survey/Mapping

xxx  Langkawi          Malaysia          06-26N 099-46E 1985-2002  99 Dept. Survey/Mapping

043  Lumut             Malaysia          04-14N 100-37E 1984-2002  97 Dept. Survey/Mapping

xxx  Penang            Malaysia          05-25N 100-21E 1984-2002  97 Dept. Survey/Mapping

030  Karachi           Pakistan          24-48N 066-58E 1985-1994  83 Nat. Inst. of Ocean.

042  Ko Taphao Noi     Thailand          07-50N 098-26E 1985-2002  97 Naval Hydro. Dept.

xxx  Lamu-A            Kenya             02-16S 040-54E 1989-1989  68 Kenya Marine Fisheries

xxx  Lamu-B            Kenya             02-16S 040-54E 1995-2003 100 UH Sea Level Center

015  Nosy Be           Madagascar        13-24S 048-18E 1987-1998  54 CNRO

297  Zanzibar          Tanzania          06-09S 039-11E 1984-2001  99 UH Sea Level Center

096  Dzaoudzi          Mayotte           12-47S 045-15E 1985-1995  67 SHOM

xxx  Meneng            Indonesia         08-07S 114-23E 1987-1989  94 Center for Ocean. Res.

xxx  Pari              Indonesia         05-51S 106-37E 1987-1990  84 Center for Ocean. Res.

292  Surabaya          Indonesia         07-13S 112-44E 1988-1990  93 BAKOSURTANAL

xxx  Jakarta           Indonesia         06-06S 106-53E 1984-1985 100 BAKOSURTANAL

049  Benoa             Indonesia         08-45S 115-13E 1988-1990  97 BAKOSURTANAL

017  Reunion           France            20-55S 055-18E 1982-1986  93 SHOM

xxx  Wyndham           Australia         15-27S 128-06E 1984-1999  97 Nat. Tidal Facility

040  Broome            Australia         18-00S 122-13E 1986-1999  78 Nat. Tidal Facility

052  Carnarvon         Australia         24-54S 113-39E 1984-1999  75 Nat. Tidal Facility

062  Darwin            Australia         12-28S 130-51E 1984-2003  97 Nat. Tidal Facility

051  Port Hedland      Australia         20-19S 118-34E 1984-1999  97 Nat. Tidal Facility

047  Christmas         Australia         10-25S 105-40E 1986-1993  52 CSIRO

046  Cocos             Australia         12-07S 096-53E 1985-2003  94 Nat. Tidal Facility

053  Fremantle         Australia         32-03S 115-43E 1984-1999  99 Nat. Tidal Facility

054  Esperance         Australia         33-52S 121-54E 1985-2003  97 Nat. Tidal Facility

021  Crozet            France            46-26S 051-52E 1995-2000  47 Inst. Mech. Grenoble

024  Saint Paul        France            38-43S 077-32E 1994-2000  87 Inst. Mech. Grenoble

023  Kerguelen         France            49-21S 070-13E 1993-1998  99 Inst. Mech. Grenoble

013  Durban            South Africa      29-53S 031-02E 1970-1996  82 Dir. of Hydrography

xxx  Mina Sulman       Bahrain           26-14N 050-36E 1979-1997  88 Survey Directorate

076  Port Elizabeth    South Africa      33-58S 025-38E 1985-1996  78 Dir. of Hydrography

xxx  Mossel Bay        South Africa      34-11S 022-08E 1991-1996  91 Dir. of Hydrography

xxx  East London       South Africa      33-01S 027-55E 1991-1996  68 Dir. of Hydrography

xxx  Richard's Bay     South Africa      28-48S 032-05E 1991-1996  47 Dir. of Hydrography

xxx  Maputo-A          Mozambique        26-10S 032-42E 1974-1974 100 Inst. Hidro. Marinha

xxx  Maputo-B          Mozambique        25-59S 032-34E 1981-1986  49 INAHINA

xxx  Antonio Enes      Mozambique        16-14S 039-54E 1967-1967  31 Inst. Hidro. Marinha

011  Pemba-A           Mozambique        12-58S 040-30E 1971-1973  25 Inst. Hidro. Marinha

011  Pemba-B           Mozambique        12-58S 040-29E 1982-1984  64 INAHINA

xxx  Nacala-A          Mozambique        14-28S 040-41E 1975-1975  18 Inst. Hidro. Marinha

xxx  Nacala-B          Mozambique        14-28S 040-41E 1982-1983 100 Inst. Hidro. Marinha

GENERAL INFORMATION FOR DESIRED STATIONS: Atlantic Ocean

# Series: 171

# Site-years: 3312

column notes:

CI: Completeness index or percentage of data span without missing data.

QC-YEARS: years which have received quality control.

GLOS STATION           COUNTRY           LAT    LONG    QC-YEARS   CI  CONTRIBUTOR

199  St. Peter&Paul R. Brazil            00-55N 029-21W 1982-1985  99 ORSTOM

197  Natal-A           Brazil            05-45S 035-12W 1982-1983 100 ORSTOM

197  Natal-B           Brazil            05-45S 035-12W 1983-1984  99 ORSTOM

197  Natal-C           Brazil            05-45S 035-12W 1984-1985 100 ORSTOM

198  Fer. de Nor.-A    Brazil            03-50S 032-24W 1982-1983 100 ORSTOM

198  Fer. de Nor.-B    Brazil            03-50S 032-24W 1984-1985 100 ORSTOM

198  Fer. de Nor.-C    Brazil            03-50S 032-24W 1985-1986 100 LPAO/INPE

265  Trindade          Brazil            20-30S 029-19W 1983-1983  16 ORSTOM

xxx  Arrecife-A        Spain             28-57N 013-34W 1959-1973  98 Inst. Espanol Ocean.

xxx  Arrecife-B        Spain             28-57N 013-34W 1973-1985  69 Inst. Espanol Ocean.

xxx  Arrecife-D        Spain             28-57N 013-34W 1987-1991  90 Inst. Espanol Ocean.

xxx  S.Cruz Palma-A    Spain             28-41N 017-45W 1949-1959 100 Inst. Espanol Ocean.

xxx  S.Cruz Palma-B    Spain             28-41N 017-45W 1959-1981  93 Inst. Espanol Ocean.

xxx  S.Cruz Palma-D    Spain             28-41N 017-45W 1989-1990  93 Inst. Espanol Ocean.

249  Ceuta-A           Spain             35-54N 005-19W 1971-1974  98 Inst. Espanol Ocean.

249  Ceuta-B           Spain             35-54N 005-19W 1975-1977  97 Inst. Espanol Ocean.

249  Ceuta-C           Spain             35-54N 005-19W 1978-1980  92 Inst. Espanol Ocean.

249  Ceuta-D           Spain             35-54N 005-19W 1980-1991  90 Inst. Espanol Ocean.

xxx  Vigo              Spain             42-14N 008-44W 1943-1990 100 Inst. Espanol Ocean.

246  Cascais           Portugal          38-42N 009-25W 1960-1991  85 Inst. Hidro. Marinha

244  Flores-A,Azores   Portugal          39-27N 031-07W 1976-1977 100 Inst. Hidro. Marinha

244  Flores-B,Azores   Portugal          39-27N 031-07W 1984-1994  63 Inst. Hidro. Marinha

245  Ponta Delgada-A   Portugal          37-44N 025-40W 1978-1991  68 Inst. Hidro. Marinha

245  Ponta Delgada-B   Portugal          37-44N 025-40W 1998-2001  98 UH Sea Level Center

xxx  Horta,Azores      Portugal          38-32N 028-37W 1984-1986  87 Inst. Hidro. Marinha

xxx  Angra Heroismo-A  Portugal          38-39N 027-14W 1957-1962 100 Inst. Hidro. Marinha

xxx  Angra Heroismo-B  Portugal          38-39N 027-14W 1976-1983  94 Inst. Hidro. Marinha

254  Porto Grande      Portugal          16-52N 024-59W 1990-1993  38 Inst. Hidro. Marinha

251  Las Palmas-A      Spain             28-06N 015-24W 1949-1956  95 Inst. Espanol Ocean.

251  Las Palmas-B      Spain             28-06N 015-24W 1971-1982  88 Inst. Espanol Ocean.

251  Las Palmas-C      Spain             28-06N 015-24W 1983-1991  73 Inst. Espanol Ocean.

251  Las Palmas-D      Spain             28-09N 015-24W 1992-1999  97 Puertos del Estado

250  Funchal-B         Portugal          32-38N 016-54W 1976-1994  59 Inst. Hidro. Marinha

267  Walvis Bay        Namibia           22-57S 014-30E 1959-1993  67 Dir. of Hydrography

268  Simon's Bay       South Africa      34-11S 018-26E 1958-1996  93 Dir. of Hydrography

xxx  Praia-A           Cape Verde        14-55N 023-30W 1984-1985 100 ORSTOM

xxx  Praia-C           Cape Verde        14-55N 023-31W 1995-1996  64 National Ocean Service

253  Dakar-A           Senegal           14-40N 017-26W 1982-1983 100 ORSTOM

253  Dakar-B           Senegal           14-40N 017-26W 1983-1985 100 ORSTOM

253  Dakar-C           Senegal           14-40N 017-26W 1986-1986  44 ORSTOM

253  Dakar-D           Senegal           14-40N 017-26W 1986-1989  94 ORSTOM

253  Dakar-E           Senegal           14-41N 017-25W 1996-2001  92 UH Sea Level Center

260  Sao Tome          Sao Tome/Principe 00-01N 006-31E 1985-1988  58 ORSTOM

xxx  Tenerife          Spain             28-29N 016-14W 1992-1999  92 Puertos del Estado

xxx  Belem             Brazil            01-27S 048-30W 1955-1968  96 National Ocean Service

257  Abidjan-Vridi     Ivory Coast       05-15N 004-00W 1982-1988 100 ORSTOM

xxx  Takoradi          Ghana             04-53N 001-45W 1983-1986 100 ORSTOM

259  Lagos-A           Nigeria           06-25N 003-27E 1961-1969  63 POL

259  Lagos-C           Nigeria           06-25N 003-25E 1992-1996  74 NIOMR

261  Pointe Noire      Congo             04-48S 011-51E 1980-1988  77 ORSTOM

xxx  Palmeira,C.Verde  Portugal          16-45N 022-59W 2000-2001  68 UH Sea Level Center

xxx  Luanda            Angola            08-47S 013-14E 1972-1975 100 Inst. Hidro. Marinha

262  Lobito            Angola            12-20S 013-34E 1971-1975  88 Inst. Hidro. Marinha

xxx  Mocamedes         Angola            15-12S 012-09E 1971-1975  98 Inst. Hidro. Marinha

xxx  Fernandina Beach  USA               30-40N 081-28W 1985-2003  91 National Ocean Service

218  Miami             USA               25-54N 080-07W 1985-1992  96 National Ocean Service

216  Key West          USA               24-33N 081-49W 1913-2003  97 National Ocean Service

276  Gibara            Cuba              21-07N 076-07W 1985-1992 100 Inst. Cubano De Hidro.

206  San Juan          USA               18-28N 066-07W 1985-2003  94 National Ocean Service

xxx  Magueyes Island   USA               17-58N 067-03W 1985-2003  97 National Ocean Service

xxx  La Guaira         Venezuela         10-37N 066-56W 1985-1994  97 Inst. Ocean. Venezuela

203  Port-of-Spain     Trinidad/Tobago   10-39N 061-31W 1984-1992  81 Trin/Tob. Hydro. Unit

xxx  Bridgetown-A      Barbados          13-06N 059-37W 1968-1970  98 National Ocean Service

xxx  Bridgetown-B      Barbados          13-06N 059-37W 1990-1991  92 Gov. of Barbados

xxx  Bridgetown-C      Barbados          13-06N 059-37W 1993-1996  45 Gov. of Barbados

212  Veracruz          Mexico            19-12N 096-08W 1985-1995  99 UNAM

xxx  Guantanamo Bay-A  Cuba              19-54N 075-09W 1937-1948  81 National Ocean Service

xxx  Guantanamo Bay-B  Cuba              19-54N 075-09W 1995-1997  89 National Ocean Service

xxx  Portland,ME       USA               43-39N 070-15W 1910-2003  97 National Ocean Service

290  Newport,RI        USA               41-30N 071-20W 1930-2003  95 National Ocean Service

xxx  Limetree Bay      USA               17-42N 064-45W 1982-2003  89 National Ocean Service

xxx  Charlotte Amalie  USA               18-20N 064-55W 1978-2003  87 National Ocean Service

012  Exuma Cays        Bahamas           23-46N 076-06W 1992-1993  99 HBOI

211  Settlement Pnt.-A Bahamas           26-43N 078-60W 1985-2002  91 National Ocean Service

211  Settlement Pnt.-B Bahamas           26-41N 078-59W 1985-2003  78 National Ocean Service

221  Bermuda           United Kingdom    32-22N 064-42W 1985-2003  78 National Ocean Service

219  Duck Pier,NC      USA               36-11N 075-45W 1978-2003  99 National Ocean Service

xxx  Charleston,SC     USA               32-47N 079-56W 1921-2003  98 National Ocean Service

xxx  St. Augustine,FL  USA               29-51N 081-16W 1978-2002  42 National Ocean Service

220  Atlantic City,NJ  USA               39-21N 074-25W 1911-2003  94 National Ocean Service

207  Cartagena-A       Colombia          10-23N 075-32W 1951-1993  90 IDEAM

207  Cartagena-B       Colombia          10-23N 075-32W 1993-2000  81 IDEAM

208  Cristobal         Panama            09-21N 079-55W 1907-1997  96 Panama Canal Commission

xxx  Limon             Costa Rica        10-00N 083-02W 1970-1981  66 SERMAR

xxx  Cochino Pequeno   Honduras          15-57N 086-30W 1995-1996 100 National Ocean Service

204  Le Robert         France            14-41N 060-56W 1976-1984  61 SHOM

xxx  Fort de France    France            14-35N 061-03W 1976-1985  37 SHOM

xxx  Pointe-a-Pitre    France            16-14N 061-32W 1991-1998  96 Meteo-France

xxx  Churchill         Canada            58-47N 094-12W 1961-2000  90 MEDS

222  Halifax           Canada            44-40N 063-35W 1920-2000  99 MEDS

223  St. John's-A      Canada            47-34N 052-42W 1961-1993  96 MEDS

223  St. John's-B      Canada            47-34N 052-42W 1993-2000  97 MEDS

xxx  Montauk           USA               41-03N 071-58W 1959-2003  90 National Ocean Service

195  Rio de Janeiro    Brazil            22-54S 043-10W 1963-2003  94 Dir. Hidro. e Navegacao

194  Cananeia          Brazil            25-01S 047-56W 1954-2000 100 Inst. Ocean. USP

xxx  Fortaleza-A       Brazil            03-43S 038-29W 1955-1968  95 National Ocean Service

xxx  Fortaleza-B       Brazil            03-43S 038-28W 1995-1998 100 LPAO/INPE

xxx  Termisa           Brazil            04-49S 037-03W 1993-1995  97 LPAO/INPE

xxx  Buenos Aires      Argentina         34-40S 058-30W 1905-1961 100 Ser. Hidro. Naval

180  Puerto Williams   Chile             54-56S 067-37W 1985-1998  88 SHOA

305  Port Stanley-A    United Kingdom    52-42S 057-52W 1964-1974  47 POL

305  Port Stanley-B    United Kingdom    51-45S 057-56W 1992-2003  90 POL

263  Ascension         United Kingdom    07-55S 014-25W 1993-2001  89 POL

264  St. Helena        United Kingdom    15-55S 005-43W 1993-2001  90 POL

236  Lerwick           United Kingdom    60-09N 001-08W 1959-2001  99 POL

241  Newlyn            United Kingdom    50-06N 005-33W 1915-2001  99 POL

238  Stornoway         United Kingdom    58-13N 006-23W 1976-2001  80 POL

xxx  Sisimiut          Denmark           66-56N 053-40W 1991-1995  93 Danish Navig./Hydro.

228  Ammassalik        Denmark           65-36N 037-00W 1990-1995  81 Danish Navig./Hydro.

xxx  Ilulissat         Denmark           69-13N 051-06W 1992-1995  90 Danish Navig./Hydro.

xxx  Qaqortoq          Denmark           60-43N 046-02W 1991-1995  99 Danish Navig./Hydro.

181  Ushuaia           Argentina         54-48S 068-18W 1996-2001  80 National Ocean Service

185  Esperanza         Argentina         63-24S 056-60W 1996-1998  86 National Ocean Service

188  Faraday           United Kingdom    65-15S 064-16W 1984-1999  98 POL

xxx  Port Nolloth      South Africa      29-15S 016-52E 1991-1994  49 Dir. of Hydrography

xxx  Luderitz          South Africa      26-39S 015-09E 1991-1996  34 Dir. of Hydrography

xxx  Saldahna Bay      South Africa      33-01S 018-58E 1991-1996  81 Dir. of Hydrography

xxx  Granger Bay       South Africa      33-54S 018-25E 1991-1996  55 Dir. of Hydrography

153  L. Cornwallis I.  Canada            75-23N 096-57W 1986-1994 100 MEDS

xxx  Canavieiras       Brazil            15-40S 038-58W 1956-1961  95 National Ocean Service

xxx  Salvador          Brazil            12-58S 038-31W 1955-1964  92 National Ocean Service

195  R.Janeiro,USCGS   Brazil            22-56S 043-08W 1955-1968  70 National Ocean Service

xxx  Suape             Brazil            08-21S 034-57W 1982-1984  98 LPAO/INPE

xxx  Luis Corriea      Brazil            02-52S 041-40W 1984-1985 100 LPAO/INPE

xxx  Recife,USCGS      Brazil            08-03S 034-52W 1955-1968  86 National Ocean Service

193  Porto Rio Grande  Brazil            32-08S 052-06W 1981-2003  22 Dir. Hidro. e Navegacao

200  Madeira           Brazil            02-34S 044-23W 1988-2003  81 Dir. Hidro. e Navegacao

201  Santana-A         Brazil            00-03S 051-11W 1970-1972 100 Dir. Hidro. e Navegacao

201  Santana-B         Brazil            00-03S 051-11W 1975-1976 100 Dir. Hidro. e Navegacao

201  Santana-C         Brazil            00-03S 051-11W 1984-1985 100 Dir. Hidro. e Navegacao

201  Santana-D         Brazil            00-03S 051-11W 1996-1997 100 Dir. Hidro. e Navegacao

201  Santana SSN-A     Brazil            00-04S 051-10W 1994-1995  99 Dir. Hidro. e Navegacao

201  Santana SSN-A     Brazil            00-04S 051-10W 1999-2000  99 Dir. Hidro. e Navegacao

xxx  Nassau            Bahamas           25-05N 077-21W 1904-1905 100 National Ocean Service

xxx  Point Fortin      Trinidad/Tobago   10-06N 061-25W 1987-1996  61 Trin/Tob. Hydro. Unit

189  Base Prat         Chile             62-29S 059-38W 1984-2002  96 SHOA

xxx  Eastport,ME       USA               44-54N 066-59W 1929-2003  93 National Ocean Service

xxx  Boston,MA         USA               42-21N 071-03W 1921-2003  99 National Ocean Service

xxx  Woods Hole,MA     USA               41-31N 070-40W 1957-2003  89 National Ocean Service

xxx  Nantucket,MA      USA               41-17N 070-06W 1965-2003  95 National Ocean Service

xxx  New London,CT     USA               41-21N 072-05W 1957-2003  93 National Ocean Service

xxx  New York,NY       USA               40-42N 074-01W 1958-2003  85 National Ocean Service

xxx  Cape May,NJ       USA               38-58N 074-58W 1965-2003  87 National Ocean Service

xxx  Lewes,DE          USA               38-47N 075-07W 1957-2003  96 National Ocean Service

xxx  Chesapeake BBT,VA USA               36-58N 076-07W 1975-2003  99 National Ocean Service

xxx  Wilmington,NC     USA               34-14N 077-57W 1935-2003  98 National Ocean Service

289  Fort Pulaski,GA   USA               32-02N 080-54W 1935-2003  95 National Ocean Service

xxx  Mayport,FL        USA               30-24N 081-26W 1928-2000  99 National Ocean Service

xxx  Cocoa Beach,FL    USA               28-22N 080-36W 1994-1996  98 National Ocean Service

xxx  Virginia Key,FL   USA               25-44N 080-10W 1996-2003  99 National Ocean Service

xxx  Naples,FL         USA               26-08N 081-48W 1996-2003  96 National Ocean Service

xxx  St. Petersburg,FL USA               27-46N 082-38W 1946-2003  96 National Ocean Service

xxx  Apalachicola,FL   USA               29-44N 084-59W 1996-2003  98 National Ocean Service

xxx  Panama City Bh,FL USA               30-13N 085-53W 1993-2001  96 National Ocean Service

288  Pensacola,FL      USA               30-24N 087-13W 1923-2003  97 National Ocean Service

xxx  Dauphin Island AL USA               30-15N 088-05W 1996-2003  47 National Ocean Service

xxx  South Pass,LA     USA               28-59N 089-08W 1993-1999  90 National Ocean Service

xxx  Grand Isle,LA     USA               29-16N 089-57W 1980-2003  99 National Ocean Service

xxx  Sabine Pass N, TX USA               29-44N 093-52W 1992-2003  99 National Ocean Service

xxx  Galveston,P.Pier  USA               29-17N 094-47W 1957-2003  96 National Ocean Service

xxx  Rockport,TX       USA               28-01N 097-03W 1987-2003  99 National Ocean Service

xxx  Corpus Cristi,TX  USA               27-35N 097-13W 1992-1999 100 National Ocean Service

xxx  Port Isabel,TX    USA               26-04N 097-13W 1977-2003  96 National Ocean Service

xxx  Clearwater Bch,FL USA               27-59N 082-50W 1996-2003  96 National Ocean Service

xxx  Port Canaveral,FL USA               28-25N 080-36W 1994-2003  98 National Ocean Service

217  Galveston,Pier21  USA               29-19N 094-48W 1904-2001  96 National Ocean Service

xxx  Puerto Cortes     Honduras          15-50N 087-57W 1948-1968  99 National Ocean Service

xxx  Belize            British Honduras  17-30N 088-11W 1964-1967  84 National Ocean Service

210  Port Royal        Jamaica           17-56N 076-51W 1965-1971  99 National Ocean Service

xxx  Fajardo,PR        USA               18-20N 065-38W 1921-1923  95 National Ocean Service

xxx  Puerto Castilla   Honduras          16-01N 086-02W 1955-1967  78 National Ocean Service